###### Chapter 06.04

###### Nonlinear Models for Regression

After reading this chapter, you should be able to

- derive constants of nonlinear regression models,

- use in examples, the derived formula for the constants of the nonlinear regression model, and

- linearize (transform) data to find constants of some nonlinear regression models.

From fundamental theories, we may know the relationship between two variables.  An example in chemical engineering is the Clausius-Clapeyron equation that relates vapor pressure  of a vapor to its absolute temperature, .

(1)

where  and  are the unknown parameters to be determined.  The above equation is not linear in the unknown parameters.  Any model that is not linear in the unknown parameters is described as a nonlinear regression model.

# Nonlinear models using least squares

The development of the least squares estimation for nonlinear models does not generally yield equations that are linear and hence easy to solve.  An example of a nonlinear regression model is the exponential model.

## Exponential model

Given , , . . . , best fit  to the data.  The variables  and  are the constants of the exponential model.  The residual at each data point  is

(2)

The sum of the square of the residuals is

(3)

To find the constants  and  of the exponential model, we minimize  by differentiating with respect to and and equating the resulting equations to zero.

(4a,b)

or

(5a,b)

Equations (5a) and (5b) are nonlinear in  and  and thus not in a closed form to be solved as was the case for linear regression.  In general, iterative methods (such as Gauss-Newton iteration method, method of steepest descent, Marquardt's method, direct search, etc) must be used to find values of  and .

However, in this case, from Equation (5a), can be written explicitly in terms of as

(6)

Substituting Equation (6) in (5b) gives

(7)

This equation is still a nonlinear equation in and can be solved best by numerical methods such as the bisection method or the secant method.

# Example 1

Many patients get concerned when a test involves injection of a radioactive material.  For example for scanning a gallbladder, a few drops of Technetium-99m isotope is used.  Half of the techritium-99m would be gone in about 6 hours.  It, however, takes about 24 hours for the radiation levels to reach what we are exposed to in day-to-day activities.  Below is given the relative intensity of radiation as a function of time.

Table 1  Relative intensity of radiation as a function of time

|  | 0 | 1 | 3 | 5 | 7 | 9 |
| --- | --- | --- | --- | --- | --- | --- |
|  | 1.000 | 0.891 | 0.708 | 0.562 | 0.447 | 0.355 |

If the level of the relative intensity of radiation is related to time via an exponential formula , find

- the value of the regression constants  and ,

- the half-life of Technium-99m, and

- the radiation intensity after 24 hours.

# Solution

a) The value of  is given by solving the nonlinear Equation (7),

(8)

and then the value of  from Equation (6),

(9)

Equation (8) can be solved for  using bisection method.  To estimate the initial guesses, we assume  and .  We need to check whether these values first bracket the root of .  At , the table below shows the evaluation of .

Table 2 Summation value for calculation of constants of model

| 1 2 3 4 5 6 | 0 1 3 5 7 9 | 1 0.891 0.708 0.562 0.447 0.355 | 0.00000 0.70719 1.0620 0.88509 0.62087 0.39937 | 1.00000 0.70719 0.35400 0.17702 0.08870 0.04437 | 1.00000 0.62996 0.25000 0.09921 0.03937 0.01562 | 0.00000 0.62996 0.75000 0.49606 0.27560 0.14062 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 3.6745 | 2.3713 | 2.0342 | 2.2922 |

From Table 2

Similarly

Since

,

the value of   falls in the bracket of .  The next guess of the root then is

Continuing with the bisection method, the root of  is found as.  This value of the root was obtained after 20 iterations with an absolute relative approximate error of less than 0.0002%.

From Equation (9),  can be calculated as

The regression formula is hence given by

b) Half life of Technetium-99m is when

c) The relative intensity of the radiation after 24 hrs is

This implies that only of the initial radioactive intensity is left after 24 hrs.

Figure 1 Relative intensity of radiation as a function of temperature using an exponential regression model.

## Growth model

Growth models common in scientific fields have been developed and used successfully for specific situations.  The growth models are used to describe how something grows with changes in the regressor variable (often the time).  Examples in this category include growth of thin films or population with time.  Growth models include

(10)

where  and  are the constants of the model. At ,  and as , .

The residuals at each data point , are

(11)

The sum of the square of the residuals is

(12)

To find the constants ,  and  we minimize  by differentiating with respect to , and , and equating the resulting equations to zero.

,

,

.		                           (13a,b,c)

One can use the Newton-Raphson method to solve the above set of simultaneous nonlinear equations for ,  and .

# Example 2

The height of a child is measured at different ages as follows.

Table 3 Height of the child at different ages.

|  | 0 | 5.0 | 8 | 12 | 16 | 18 |
| --- | --- | --- | --- | --- | --- | --- |
|  | 20 | 36.2 | 52 | 60 | 69.2 | 70 |

Estimate the height of the child as an adult of 30 years of age using the growth model,

# Solution

The saturation growth model of height,  vs. age,  is given as

where the constants ,  and  are the roots of the simultaneous nonlinear equation system

(14a,b,c)

We need initial guesses of the roots to get the iterative process started to find the root of those equations. Suppose we use three of the given data points such as (0, 20), (12, 60) and (18, 70) to find the initial guesses of roots; we have

One can solve three unknowns ,  and  from the three equations as

Applying the Newton-Raphson method for simultaneous nonlinear equations, one can get the roots

The saturation growth model of the height of the child then is

The height of the child as an adult of 30 years of age is

## Polynomial Models

Given  data points  use least squares method to regress the data to an  order polynomial.

(15)

The residual at each data point is given by

(16)

The sum of the square of the residuals is given by

(17)

To find the constants of the polynomial regression model, we put the derivatives with respect to  to zero, that is,

Figure 2 Height of child as a function of age saturation growth model.

(18)

Setting those equations in matrix form gives

(19)

The above are solved for

# Example 3

To find contraction of a steel cylinder, one needs to regress the thermal expansion coefficient data to temperature

Table 4 The thermal expansion coefficient at given different temperatures

| Temperature, | Coefficient of thermal expansion, |
| --- | --- |
| 80 |  |
| 40 |  |
| -40 |  |
| -120 |  |
| -200 |  |
| -280 |  |
| -340 |  |

Fit the above data to

#### Solution

Since  is the quadratic relationship between the thermal expansion coefficient and the temperature, the coefficients  are found as follows

Table 5 Summations for calculating constants of model

| 1 | 80 |  |  |  |
| --- | --- | --- | --- | --- |
| 2 | 40 |  |  |  |
| 3 | -40 |  |  |  |
| 4 | -120 |  |  |  |
| 5 | -200 |  |  |  |
| 6 | -280 |  |  |  |
| 7 | -340 |  |  |  |

Table 5 (cont)

| 1 |  |  |  |
| --- | --- | --- | --- |
| 2 |  |  |  |
| 3 |  |  |  |
| 4 |  |  |  |
| 5 |  |  |  |
| 6 |  |  |  |
| 7 |  |  |  |

We have

Solving the above system of simultaneous linear equations, we get

The polynomial regression model is

# Transforming the data to use linear regression formulas

Examination of the nonlinear models above shows that in general iterative methods are required to estimate the values of the model parameters.  It is sometimes useful to use simple linear regression formulas to estimate the parameters of a nonlinear model.  This involves first transforming the given data such as to regress it to a linear model.  Following the transformation of the data, the evaluation of model parameters lends itself to a direct solution approach using the least squares method.  Data for nonlinear models such as exponential, power, and growth can be transformed.

## Exponential Model

As given in Example 1, many physical and chemical processes are governed by the exponential function.

(20)

Taking natural log of both sides of Equation (20) gives

(21)

Let

implying

then

(22)

Figure 3 Second-order polynomial regression model for coefficient of thermal expansion as a function of temperature.

The data  versus  is now a linear model. The constants  and  can be found using the equation for the linear model as

(23a,b)

Now since  and  are found, the original constants with the model are found as

(24a,b)

# Example 4

Repeat Example 1 using linearization of data.

# Solution

Assuming

We get

This is a linear relationship between  and .

(25a,b)

Table 6 Summations of data to calculate constants of model.

| 1 2 3 4 5 6 | 0 1 3 5 7 9 | 1 0.891 0.708 0.562 0.447 0.355 | 0.00000 -0.11541 -0.34531 -0.57625 -0.80520 -1.0356 | 0.0000 -0.11541 -1.0359 -2.8813 -5.6364 -9.3207 | 0.0000 1.0000 9.0000 25.000 49.000 81.000 |
| --- | --- | --- | --- | --- | --- |
|  | 25.000 |  | -2.8778 | -18.990 | 165.00 |

From Equation (25a,b) we have

Since

The regression formula then is

Compare the formula to the one obtained without data linearization,

b) Half-life is when

c) The relative intensity of radiation, after 24 hours is

This implies that only of the initial radioactivity is left after 24 hours.

## Logarithmic Functions

The form for the log regression models is

(26)

This is a linear function between  and  and the usual least squares method applies in which  is the response variable and  is the regressor.

Figure 4 Exponential regression model with transformed data for relative intensity of radiation as a function of temperature.

# Example 5

Sodium borohydride is a potential fuel for fuel cell. The following overpotential  vs. current data was obtained in a study conducted to evaluate its electrochemical kinetics.

Table 7 Electrochemical Kinetics of borohydride data.

|  | -0.29563 | -0.24346 | -0.19012 | -0.18772 | -0.13407 | -0.0861 |
| --- | --- | --- | --- | --- | --- | --- |
|  | 0.00226 | 0.00212 | 0.00206 | 0.00202 | 0.00199 | 0.00195 |

At the conditions of the study, it is known that the relationship that exists between the overpotential  and current  can be expressed as

(27)

where  is an electrochemical kinetics parameter of borohydride on the electrode. Use the data in Table 7 to evaluate the values of  and.

# Solution

Following the least squares method, Table 8 is tabulated where

We obtain

(28)

This is a linear relationship between  and , and the coefficients  and  are found as follow

(29a,b)

Table 8 Summation values for calculating constants of model

| # |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 1 | 0.00226 | -0.29563 | -6.0924 | 37.117 | 1.8011 |
| 2 | 0.00212 | -0.24346 | -6.1563 | 37.901 | 1.4988 |
| 3 | 0.00206 | -0.19012 | -6.1850 | 38.255 | 1.1759 |
| 4 | 0.00202 | -0.18772 | -6.2047 | 38.498 | 1.1647 |
| 5 | 0.00199 | -0.13407 | -6.2196 | 38.684 | 0.83386 |
| 6 | 0.00195 | -0.08610 | -6.2399 | 38.937 | 0.53726 |
|  | 0.012400 | -1.1371 | -37.098 | 229.39 | 7.0117 |

Hence

Figure 5 Overpotential as a function of current.

## Power Functions

The power function equation describes many scientific and engineering phenomena. In chemical engineering, the rate of chemical reaction is often written in power function form as

(30)

The method of least squares is applied to the power function by first linearizing the data (the assumption is that  is not known). If the only unknown is, then a linear relation exists between  and. The linearization of the data is as follows.

(31)

The resulting equation shows a linear relation between  and .

Let

implying

we get

(32)

(33a,b)

Since  and  can be found, the original constants of the model are

(34a,b)

# Example 6

The progress of a homogeneous chemical reaction is followed and it is desired to evaluate the rate constant and the order of the reaction. The rate law expression for the reaction is known to follow the power function form

(35)

Use the data provided in the table to obtain  and .

Table 9 Chemical kinetics.

|  | 4 | 2.25 | 1.45 | 1.0 | 0.65 | 0.25 | 0.006 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0.398 | 0.298 | 0.238 | 0.198 | 0.158 | 0.098 | 0.048 |

# Solution

Taking the natural log of both sides of Equation (35), we obtain

Let

implying that 			     		                       (36)

(37)

We get

This is a linear relation between  and , where

(38a,b)

Table 10 Kinetics rate law using power function

| 1 | 4 | 0.398 | 1.3863 | -0.92130 | -1.2772 | 1.9218 |
| --- | --- | --- | --- | --- | --- | --- |
| 2 | 2.25 | 0.298 | 0.8109 | -1.2107 | -0.9818 | 0.65761 |
| 3 | 1.45 | 0.238 | 0.3716 | -1.4355 | -0.5334 | 0.13806 |
| 4 | 1 | 0.198 | 0.0000 | -1.6195 | 0.0000 | 0.00000 |
| 5 | 0.65 | 0.158 | -0.4308 | -1.8452 | 0.7949 | 0.18557 |
| 6 | 0.25 | 0.098 | -1.3863 | -2.3228 | 3.2201 | 1.9218 |
| 7 | 0.006 | 0.048 | -5.1160 | -3.0366 | 15.535 | 26.173 |
|  |  |  | -4.3643 | -12.391 | 16.758 | 30.998 |

From Equation (38a,b)

From Equation (36) and (37), we obtain

Finally, the model of progress of that chemical reaction is

Figure 6 Kinetic chemical reaction rate as a function of concentration.

## Growth Model

Growth models common in scientific fields have been developed and used successfully for specific situations.  The growth models are used to describe how something grows with changes in a regressor variable (often the time).  Examples in this category include growth of thin films or population with time.  In the logistic growth model, an example of a growth model in which a measurable quantity  varies with some quantity  is

(39)

For ,  while as , .  To linearize the data for this method,

(40)

Let

,

implying that

implying

Then

(41)

The relationship between  and  is linear with the coefficients  and found as follows.

(42a,b)

Finding  and , then gives the constants of the original growth model as

(43a,b)

| NONLINEAR REGRESSION |  |
| --- | --- |
| Topic | Nonlinear Regression |
| Summary | Textbook notes of Nonlinear Regression |
| Major | Civil Engineering |
| Authors | Egwu Kalu, Autar Kaw, Cuong Nguyen |
| Date | September 10, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |