###### Chapter 03.03

###### Bisection Method of Solving a Nonlinear Equation

After reading this chapter, you should be able to:

- follow the algorithm of the bisection method of solving a nonlinear equation,

- use the bisection method to solve examples of finding roots of a nonlinear equation, and

- enumerate the advantages and disadvantages of the bisection method.

# What is the bisection method and what is it based on?

One of the first numerical methods developed to find the root of a nonlinear equation  was the bisection method (also called binary-search method).  The method is based on the following theorem.

Theorem

An equation, where  is a real continuous function, has at least one root between  and  if  (See Figure 1).

Note that if , there may or may not be any root between  and  (Figures 2 and 3).  If , then there may be more than one root between  and  (Figure 4).  So the theorem only guarantees one root between  and .

Bisection method

Since the method is based on finding the root between two points, the method falls under the category of bracketing methods.

Since the root is bracketed between two points,  and , one can find the mid-point,  between  and .  This gives us two new intervals

- and , and

- and .

Figure 1 At least one root exists between the two points if the function is real, continuous, and changes sign.

Figure 2 If the function does not change sign between the two points, roots of the equation may still exist between the two points.

Figure 3 If the function does not change sign between two points, there may not be any roots for the equation between the two points.

Figure 4   If the function  changes sign between the two points, more than one root for the equation  may exist between the two points.

Is the root now between  and  or between  and ?  Well, one can find the sign of , and if  then the new bracket is between  and , otherwise, it is between  and .  So, you can see that you are literally halving the interval.  As one repeats this process, the width of the interval  becomes smaller and smaller, and you can zero in to the root of the equation .  The algorithm for the bisection method is given as follows.

# Algorithm for the bisection method

The steps to apply the bisection method to find the root of the equation  are

- Choose  and  as two guesses for the root such that, or in other words,  changes sign between  and .

- Estimate the root, , of the equation  as the mid-point between  and  as

- Now check the following

- If , then the root lies between  and ; then  and .

- If , then the root lies between  and ; then  and .

- If ; then the root is .  Stop the algorithm if this is true.

- Find the new estimate of the root

Find the absolute relative approximate error as

where

= estimated root from present iteration

= estimated root from previous iteration

- Compare the absolute relative approximate error  with the pre-specified relative error tolerance .  If , then go to Step 3, else stop the algorithm.  Note one should also check whether the number of iterations is more than the maximum number of iterations allowed.  If so, one needs to terminate the algorithm and notify the user about it.

# Example 1

A trunnion has to be cooled before it is shrink fitted into a steel hub.

Figure 5 Trunnion to be slid through the hub after contracting.

The equation that gives the temperature  to which the trunnion has to be cooled to obtain the desired contraction is given by

Use the bisection method of finding roots of equations to find the temperature  to which the trunnion has to be cooled. Conduct three iterations to estimate the root of the above equation. Find the absolute relative approximate error at the end of each iteration and the number of significant digits at least correct at the end of each iteration.

# Solution

From the designer’s records for the previous bridge, the temperature to which the trunnion was cooled was . Hence assuming the temperature to be between and

, we have

,

Check if the function changes sign between  and .

Hence

So there is at least one root between  and  that is between  and .

## Iteration 1

The estimate of the root is

Hence the root is bracketed between  and , that is, between  and .

So, the lower and upper limits of the new bracket are

At this point, the absolute relative approximate error  cannot be calculated, as we do not have a previous approximation.

## Iteration 2

The estimate of the root is

Hence, the root is bracketed between  and , that is, between  and .

So the lower and upper limits of the new bracket are

The absolute relative approximate error  at the end of Iteration 2 is

None of the significant digits are at least correct in the estimated root of

as the absolute relative approximate error is greater that .

## Iteration 3

The estimate of the root is

Hence, the root is bracketed between  and , that is, between  and .

So the lower and upper limits of the new bracket are

The absolute relative approximate error  at the ends of Iteration 3 is

The number of significant digits at least correct is 1.

Seven more iterations were conducted and these iterations are shown in the Table 1 below.

Table 1 Root of as function of number of iterations for bisection method.

Iteration 1 2 3 4 5 6 7 8 9 10 −150 −150 −137.5 −131.25 −131.25 −129.69 −128.91 −128.91 −128.91 −128.81 −100 −125 −125 −125 −128.13 −123.13 −123.13 −128.52 −128.71 −128.71 −125 −137.5 −131.25 −128.13 −129.69 −128.91 −128.52 −128.71 −128.81 −128.76 --------- 9.0909 4.7619 2.4390 1.2048 0.60606 0.30395 0.15175 0.075815 0.037922

At the end of the iteration,

Hence, the number of significant digits at least correct is given by the largest value of  for which

So

The number of significant digits at least correct in the estimated root of  is 3.

# Advantages of bisection method

- The bisection method is always convergent.  Since the method brackets the root, the method is guaranteed to converge.

- As iterations are conducted, the interval gets halved.   So one can guarantee the error in the solution of the equation.

# Drawbacks of bisection method

- The convergence of the bisection method is slow as it is simply based on halving the interval.

- If one of the initial guesses is closer to the root, it will take larger number of iterations to reach the root.

- If a function  is such that it just touches the -axis (Figure 6) such as

it will be unable to find the lower guess, , and upper guess, , such that

- For functions  where there is a singularity and it reverses sign at the singularity, the bisection method may converge on the singularity (Figure 7).  An example includes

where ,  are valid initial guesses which satisfy

However, the function is not continuous and the theorem that a root exists is also not applicable.

| Figure 6 The equation has a single root at that cannot be bracketed. |
| --- |
| A singularity in a function is defined as a point where the function becomes infinite. For example, for a function such as , the point of singularity is as it becomes infinite. |
| Figure 7 The equation has no root but changes sign. |
| NONLINEAR EQUATIONS |  |
| Topic | Bisection Method-More Examples |
| Summary | Textbook notes on the bisection method of finding roots of nonlinear equations, including convergence and pitfalls. |
| Major | Mechanical Engineering |
| Authors | Autar Kaw |
| Date | November 15, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

f (x)

xℓ

xu

x

f (x)

xℓ

xu

x

f (x)

xℓ

xu

x

f (x)

xℓ

xu

x

f (x)

xℓ

xu

x

f (x)

x

f (x)

x