###### Multiple-Choice Test

###### Chapter 02.03

###### Differentiation of Discrete Functions

- The definition of the first derivative of a function  is

- Using the forward divided difference approximation with a step size of 0.2, the derivative of the function at  is given as

|  | 1.8 | 2.0 | 2.2 | 2.4 | 2.6 |
| --- | --- | --- | --- | --- | --- |
|  | 6.0496 | 7.3890 | 9.0250 | 11.023 | 13.464 |

- 6.697

7.389

7.438

8.180

- A student finds the numerical value of  at  using a step size of 0.2.  Which of the following methods did the student use to conduct the differentiation if  is given in the table below?

|  | 2.6 | 2.8 | 3.0 | 3.2 | 3.4 | 3.6 |
| --- | --- | --- | --- | --- | --- | --- |

- Backward divided difference

Calculus, that is, exact

Central divided difference

Forward divided difference

- The upward velocity of a body is given as a function of time as

|  | 10 | 15 | 20 | 22 |
| --- | --- | --- | --- | --- |
|  | 22 | 36 | 57 | 10 |

To find the acceleration at s, a scientist finds a second order polynomial 	approximation for the velocity, and then differentiates it to find the acceleration.  The 	estimate of the acceleration in at s is most nearly

- The velocity of a rocket is given as a function of time as

|  | 0 | 0.5 | 1.2 | 1.5 | 1.8 |
| --- | --- | --- | --- | --- | --- |
|  | 0 | 213 | 223 | 275 | 300 |

Allowed to use the forward divided difference, backward divided difference or central divided difference approximation of the first derivative, your best estimate for the acceleration of the rocket in  at  seconds is

- In a circuit with an inductor of inductance , a resistor with resistance , and a variable voltage source ,

The current, , is measured at several values of time as

| Time, (secs) | 1.00 | 1.01 | 1.03 | 1.1 |
| --- | --- | --- | --- | --- |
| Current, (amperes) | 3.10 | 3.12 | 3.18 | 3.24 |

If  henries and  ohms, the most accurate expression for  is

For a complete solution, refer to the links at the end of the book.