###### Multiple-Choice Test

###### Chapter 08.07

###### Finite Difference Method

- The exact solution to the boundary value problem

, ,

for  is

0.00

16.000

37.333

- Given

, ,

the value of  at  using the finite difference method and a step size of   can be approximated by

- Given

, , ,

the value of  using the finite difference method with a second order accurate central 	divided difference method and a step size of  is

- 0.000

37.333

- The transverse deflection  of a cable of length  that is fixed at both ends, is given as a solution to

where

= tension in cable

= flexural stiffness

= distributed transverse load

Given , , , and

Using finite difference method modeling with second order central divided difference accuracy and a step size of , the value of the deflection at the center of the cable most nearly is

- 0.072737″

0.080832″

0.081380″

0.084843″

- The radial displacement u of a pressurized hollow thick cylinder (inner radius = 5″, outer radius = 8″) is given at different radial locations.

| Radius (in) | Radial Displacement (in) |
| --- | --- |
| 5.0 | 0.0038731 |
| 5.6 | 0.0036165 |
| 6.2 | 0.0034222 |
| 6.8 | 0.0032743 |
| 7.4 | 0.0031618 |
| 8.0 | 0.0030769 |

The maximum normal stress, in psi, on the cylinder is given by

The maximum stress, in psi, with second order accuracy is

- 2079.6

- 2104.5

- 2130.7

- 2182.0

- For a simply supported beam (at  and ) with a uniform load q, the vertical deflection  is described by the boundary value ordinary differential equation as 		,

where

= Young’s modulus of the beam

= second moment of area

This ordinary differential equation is based on assuming that  is small.  If  is 	not small, then the ordinary differential equation is given by

For a complete solution, refer to the links at the end of the book.