###### Chapter 04.08

###### Gauss-Seidel Method

After reading this chapter, you should be able to:

- solve a set of equations using the Gauss-Seidel method,

- recognize the advantages and pitfalls of the Gauss-Seidel method, and

- determine under what conditions the Gauss-Seidel method always converges.

# Why do we need another method to solve a set of simultaneous linear equations?

In certain cases, such as when a system of equations is large, iterative methods of solving equations are more advantageous.  Elimination methods, such as Gaussian elimination, are prone to large round-off errors for a large set of equations.  Iterative methods, such as the Gauss-Seidel method, give the user control of the round-off error.  Also, if the physics of the problem are well known, initial guesses needed in iterative methods can be made more judiciously leading to faster convergence.

What is the algorithm for the Gauss-Seidel method?  Given a general set of  equations and  unknowns, we have

.                 .

.                 .

.                 .

If the diagonal elements are non-zero, each equation is rewritten for the corresponding unknown, that is, the first equation is rewritten with  on the left hand side, the second equation is rewritten with  on the left hand side and so on as follows

These equations can be rewritten in a summation form as

.

.

.

Hence for any row ,

Now to find ’s, one assumes an initial guess for the ’s and then uses the rewritten equations to calculate the new estimates.  Remember, one always uses the most recent estimates to calculate the next estimates, .  At the end of each iteration, one calculates the absolute relative approximate error for each  as

where is the recently obtained value of , and  is the previous value of .

When the absolute relative approximate error for each xi is less than the pre-specified tolerance, the iterations are stopped.

# Example 1

A liquid-liquid extraction process conducted in the Electrochemical Materials Laboratory involved the extraction of nickel from the aqueous phase into an organic phase. A typical set of experimental data from the laboratory is given below.

| Ni aqueous phase, | 2 | 2.5 | 3 |
| --- | --- | --- | --- |
| Ni organic phase, | 8.57 | 10 | 12 |

Assuming  is the amount of Ni in the organic phase and  is the amount of Ni in the aqueous phase, the quadratic interpolant that estimates  is given by

The solution for the unknowns , , and  is given by

Find the values of , , and  using the Gauss-Seidel method.   Estimate the amount of nickel in the organic phase when 2.3 g/l is in the aqueous phase using quadratic interpolation. Use

as the initial guess and conduct two iterations.

# Solution

Rewriting the equations gives

## Iteration #1

Given the initial guess of the solution vector as

we get

The absolute relative approximate error for each then is

At the end of the first iteration, the estimate of the solution vector is

and the maximum absolute relative approximate error is .

## Iteration #2

The estimate of the solution vector at the end of Iteration #1 is

Now we get

The absolute relative approximate error for each  then is

At the end of the second iteration, the estimate of the solution vector is

and the maximum absolute relative approximate error is .

Conducting more iterations gives the following values for the solution vector and the corresponding absolute relative approximate errors.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1 2 3 4 5 6 | 1.3925 2.3053 3.9775 7.0584 12.752 23.291 | 28.1867 39.5960 42.041 43.649 44.649 45.249 | 0.11875 –1.4078 –4.1340 –9.0877 –18.175 –34.930 | 742.1053 108.4353 65.946 54.510 49.999 47.967 | –0.88875 –4.5245 –11.396 –24.262 –48.243 –92.827 | 212.52 80.357 60.296 53.032 49.708 48.030 |

After six iterations, the absolute relative approximate errors are not decreasing much. In fact, conducting more iterations reveals that the absolute relative approximate error converges to a value of  for all three values with the solution vector diverging from the exact solution drastically.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |

The exact solution vector is

To correct this, the coefficient matrix needs to be more diagonally dominant. To achieve a more diagonally dominant coefficient matrix, rearrange the system of equations by exchanging equations one and three.

## Iteration #1

Given the initial guess of the solution vector as

we get

The absolute relative approximate error for each  then is

At the end of the first iteration, the estimate of the solution vector is

and the maximum absolute relative approximate error is .

## Iteration #2

The estimate of the solution vector at the end of Iteration #1 is

Now we get

The absolute relative approximate error for each  then is

At the end of the second iteration, the estimate of the solution is

and the maximum absolute relative approximate error is .

Conducting more iterations gives the following values for the solution vector and the corresponding absolute relative approximate errors.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1 2 3 4 5 6 | 0.88889 0.62309 0.48707 0.42178 0.39494 0.38890 | 12.5 42.659 27.926 15.479 6.7960 1.5521 | 1.3778 1.5387 1.5822 1.5627 1.5096 1.4393 | 27.419 10.456 2.7506 1.2537 3.5131 4.8828 | 2.2589 3.0002 3.4572 3.7576 3.9710 4.1357 | 55.730 24.709 13.220 7.9928 5.3747 3.9826 |

After six iterations, the absolute relative approximate errors seem to be decreasing. Conducting more iterations allows the absolute relative approximate error decrease to an acceptable level.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 199 200 | 1.1335 1.1337 | 0.014412 0.014056 | –2.2389 –2.2397 | 0.034871 0.034005 | 8.5139 8.5148 | 0.010666 0.010403 |

This is close to the exact solution vector of

The polynomial that passes through the three data points is then

where  is the amount of nickel in the organic phase and  is the amount of nickel in the aqueous phase.

When  is in the aqueous phase, using quadratic interpolation, the estimated amount of nickel in the organic phase is

# The above system of equations does not seem to converge.  Why?

Well, a pitfall of most iterative methods is that they may or may not converge.  However, the solution to a certain classes of systems of simultaneous equations does always converge using the GaussSeidal-Seidel method.  This class of system of equations is where the coefficient matrix  in  is diagonally dominant, that is

for all

for at least one

If a system of equations has a coefficient matrix that is not diagonally dominant, it may or may not converge.  Fortunately, many physical systems that result in simultaneous linear equations have a diagonally dominant coefficient matrix, which then assures convergence for iterative methods such as the GaussSeidal-Seidel method of solving simultaneous linear equations.

# Example 2

Find the solution to the following system of equations using the Gauss-Seidel method.

Use

as the initial guess and conduct two iterations.

# Solution

The coefficient matrix

is diagonally dominant as

and the inequality is strictly greater than for at least one row.  Hence, the solution should converge using the Gauss-Seidel method.

Rewriting the equations, we get

Assuming an initial guess of

## Iteration #1

The absolute relative approximate error at the end of the first iteration is

The maximum absolute relative approximate error is 100.00%

## Iteration #2

At the end of second iteration, the absolute relative approximate error is

The maximum absolute relative approximate error is 240.61%.  This is greater than the value of 100.00% we obtained in the first iteration.  Is the solution diverging?  No, as you conduct more iterations, the solution converges as follows.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1 2 3 4 5 6 | 0.50000 0.14679 0.74275 0.94675 0.99177 0.99919 | 100.00 240.61 80.236 21.546 4.5391 0.74307 | 4.9000 3.7153 3.1644 3.0281 3.0034 3.0001 | 100.00 31.889 17.408 4.4996 0.82499 0.10856 | 3.0923 3.8118 3.9708 3.9971 4.0001 4.0001 | 67.662 18.874 4.0064 0.65772 0.074383 0.00101 |

This is close to the exact solution vector of

# Example 3

Given the system of equations

find the solution using the Gauss-Seidel method.  Use

as the initial guess.

# Solution

Rewriting the equations, we get

Assuming an initial guess of

the next six iterative values are given in the table below.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1 2 3 4 5 6 | 21.000 –196.15 1995.0 –20149 2.0364105 –2.0579106 | 95.238 110.71 109.83 109.90 109.89 109.89 | 0.80000 14.421 –116.02 1204.6 –12140 1.2272105 | 100.00 94.453 112.43 109.63 109.92 109.89 | 50.680 –462.30 4718.1 –47636 4.8144105 –4.8653106 | 98.027 110.96 109.80 109.90 109.89 109.89 |

You can see that this solution is not converging and the coefficient matrix is not diagonally dominant.  The coefficient matrix

is not diagonally dominant as

Hence, the Gauss-Seidel method may or may not converge.

However, it is the same set of equations as the previous example and that converged.  The only difference is that we exchanged first and the third equation with each other and that made the coefficient matrix not diagonally dominant.

Therefore, it is possible that a system of equations can be made diagonally dominant if one exchanges the equations with each other.  However, it is not possible for all cases.  For example, the following set of equations

cannot be rewritten to make the coefficient matrix diagonally dominant.

# Key Terms:

Gauss-Seidel method

Convergence of Gauss-Seidel method

Diagonally dominant matrix

| SIMULTANEOUS LINEAR EQUATIONS |  |
| --- | --- |
| Topic | Gauss-Seidel Method – More Examples |
| Summary | Textbook notes of the Gauss-Seidel method |
| Major | Chemical Engineering |
| Authors | Autar Kaw |
| Date | November 3, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |