###### Chapter 05.03

###### Newton’s Divided Difference Interpolation

After reading this chapter, you should be able to:

- derive Newton’s divided difference method of interpolation,

- apply Newton’s divided difference method of interpolation, and

- apply Newton’s divided difference method interpolants to find derivatives and integrals.

# What is interpolation?

Many times, data is given only at discrete points such as  , , .  So, how then does one find the value of  at any other value of ?  Well, a continuous function  may be used to represent the  data values with  passing through the  points (Figure 1).  Then one can find the value of  at any other value of .  This is called interpolation.

Of course, if  falls outside the range of  for which the data is given, it is no longer interpolation but instead is called extrapolation.

So what kind of function  should one choose?  A polynomial is a common choice for an interpolating function because polynomials are easy to

evaluate,

differentiate, and

integrate,

relative to other choices such as a trigonometric and exponential series.

Polynomial interpolation involves finding a polynomial of order  that passes through the  points.  One of the methods of interpolation is called Newton’s divided difference polynomial method.  Other methods include the direct method and the Lagrangian interpolation method.  We will discuss Newton’s divided difference polynomial method in this chapter.

# Newton’s Divided Difference Polynomial Method

To illustrate this method, linear and quadratic interpolation is presented first.  Then, the general form of Newton’s divided difference polynomial method is presented.  To illustrate the general form, cubic interpolation is shown in Figure 1.

Figure 1 Interpolation of discrete data.

Linear Interpolation

Given  and  fit a linear interpolant through the data.  Noting  and , assume the linear interpolant  is given by (Figure 2)

Since at ,

and at ,

giving

So

giving the linear interpolant as

Figure 2 Linear interpolation.

# Example 1

To find how much heat is required to bring a kettle of water to its boiling point, you are asked to calculate the specific heat of water at . The specific heat of water is given as a  function of time in Table 1.

Table 1  Specific heat of water as a function of temperature.

| Temperature, | Specific heat, |
| --- | --- |
| 22 42 52 82 100 | 4181 4179 4186 4199 4217 |

Figure 3 Specific heat of water vs. temperature.

Determine the value of the specific heat at  using Newton’s divided difference method of interpolation and a first order polynomial.

# Solution

For linear interpolation, the specific heat is given by

Since we want to find the velocity at , and we are using a first order polynomial we need to choose the two data points that are closest to  that also bracket  to evaluate it. The two points are  and .

Then

gives

Hence

At ,

If we expand

we get

and this is the same expression as obtained in the direct method.

## Quadratic Interpolation

Given   and  fit a quadratic interpolant through the data.  Noting    and assume the quadratic interpolant  is given by

At ,

At

giving

At

Giving

Hence the quadratic interpolant is given by

Figure 4 Quadratic interpolation.

# Example 2

To find how much heat is required to bring a kettle of water to its boiling point, you are asked to calculate the specific heat of water at . The specific heat of water is given as a function of time in Table 2.

Table 2  Specific heat of water as a function of temperature.

| Temperature, | Specific heat, |
| --- | --- |
| 22 42 52 82 100 | 4181 4179 4186 4199 4217 |

Determine the value of the specific heat at  using Newton’s divided difference method of interpolation and a second order polynomial. Find the absolute relative approximate error for the second order polynomial approximation.

# Solution

For quadric interpolation, the specific heat is given by

Since we want to find the specific heat at , and we are using a second order polynomial, we need to choose the three data points that are closest to  that also bracket  to evaluate it. The three points are   and .

Then

gives

Hence

At

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

If we expand

we get

This is the same expression obtained by the direct method.

# General Form of Newton’s Divided Difference Polynomial

In the two previous cases, we found linear and quadratic interpolants for Newton’s divided difference method.  Let us revisit the quadratic polynomial interpolant formula

where

Note that  and  are finite divided differences. and  are the first, second, and third finite divided differences, respectively.  We denote the first divided difference by

the second divided difference by

and the third divided difference by

where  and  are called bracketed functions of their variables enclosed in square brackets.

Rewriting,

This leads us to writing the general form of the Newton’s divided difference polynomial for  data points, , as

where

where the definition of the  divided difference is

From the above definition, it can be seen that the divided differences are calculated recursively.

For an example of a third order polynomial, given    and

Figure 5 Table of divided differences for a cubic polynomial.

# Example 3

To find how much heat is required to bring a kettle of water to its boiling point, you are asked to calculate the specific heat of water at . The specific heat of water is given as a function of time in Table 3.

Table 3  Specific heat of water as a function of temperature.

| Temperature, | Specific heat, |
| --- | --- |
| 22 42 52 82 100 | 4181 4179 4186 4199 4217 |

Determine the value of the specific heat at  using Newton’s divided difference method of interpolation and a third order polynomial. Find the absolute relative approximate error for the third order polynomial approximation.

# Solution

For a third order polynomial, the specific heat profile is given by

Since we want to find the specific heat at , and we are using a third order polynomial, we need to choose the four data points that are closest to  that also bracket . The four data points are    and .

(Choosing the four points as , ,  and  is equally valid.)

then

Hence

At

The absolute relative approximate error  obtained between the results from the second and third order polynomial is

If we expand

we get

This is the same expression as obtained in the direct method.

| INTERPOLATION |  |
| --- | --- |
| Topic | Newton’s Divided Difference Interpolation |
| Summary | Textbook notes on Newton’s divided difference interpolation. |
| Major | Chemical Engineering |
| Authors | Autar Kaw, Michael Keteltas |
| Last Revised | November 8, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |