###### Chapter 06.03

###### Linear Regression

After reading this chapter, you should be able to

- define regression,

- use several minimizing of residual criteria to choose the right criterion,

- derive the constants of a linear regression model based on least squares method criterion,

- use in examples, the derived formulas for the constants of a linear regression model, and

- prove that the constants of the linear regression model are unique and correspond to a minimum.

Linear regression is the most popular regression model.  In this model, we wish to predict response to  data points  by a regression model given by

(1)

where  and  are the constants of the regression model.

A measure of goodness of fit, that is, how well  predicts the response variable  is the magnitude of the residual  at each of the  data points.

(2)

Ideally, if all the residuals  are zero, one may have found an equation in which all the points lie on the model.  Thus, minimization of the residual is an objective of obtaining regression coefficients.

The most popular method to minimize the residual is the least squares methods, where the estimates of the constants of the models are chosen such that the sum of the squared residuals is minimized, that is minimize .

Why minimize the sum of the square of the residuals?  Why not, for instance, minimize the sum of the residual errors or the sum of the absolute values of the residuals?  Alternatively, constants of the model can be chosen such that the average residual is zero without making individual residuals small.  Will any of these criteria yield unbiased parameters with the smallest variance?  All of these questions will be answered below.  Look at the data in Table 1.

Table 1   Data points.

| 2.0 | 4.0 |
| --- | --- |
| 3.0 | 6.0 |
| 2.0 | 6.0 |
| 3.0 | 8.0 |

To explain this data by a straight line regression model,

(3)

and using minimizing as a criteria to find  and , we find that for (Figure 1)

(4)

Figure 1 Regression curve for vs. data.

the sum of the residuals,  as shown in the Table 2.

Table 2  The residuals at each data point for regression model .

| 2.0 | 4.0 | 4.0 | 0.0 |
| --- | --- | --- | --- |
| 3.0 | 6.0 | 8.0 | -2.0 |
| 2.0 | 6.0 | 4.0 | 2.0 |
| 3.0 | 8.0 | 8.0 | 0.0 |

So does this give us the smallest error? It does as . But it does not give unique values for the parameters of the model. A straight-line of the model

(5)

also makes as shown in the Table 3.

Table 3  The residuals at each data point for regression model

| 2.0 | 4.0 | 6.0 | -2.0 |
| --- | --- | --- | --- |
| 3.0 | 6.0 | 6.0 | 0.0 |
| 2.0 | 6.0 | 6.0 | 0.0 |
| 3.0 | 8.0 | 6.0 | 2.0 |

Figure 2 Regression curve for vs. data.

Since this criterion does not give a unique regression model, it cannot be used for finding the regression coefficients. Let us see why we cannot use this criterion for any general data.  We want to minimize

(6) Differentiating Equation (6) with respect to  and , we get

(7)

(8)

Putting these equations to zero, give  but that is not possible.  Therefore, unique values of  and  do not exist.

You may think that the reason the minimization criterion does not work is that negative residuals cancel with positive residuals.  So is minimizing  better?  Let us look at the data given in the Table 2 for equation .  It makes  as shown in the following table.

Table 4   The absolute residuals at each data point when employing .

| 2.0 | 4.0 | 4.0 | 0.0 |
| --- | --- | --- | --- |
| 3.0 | 6.0 | 8.0 | 2.0 |
| 2.0 | 6.0 | 4.0 | 2.0 |
| 3.0 | 8.0 | 8.0 | 0.0 |

The value of  also exists for the straight line model . No other straight line model for this data has.  Again, we find the regression coefficients are not unique, and hence this criterion also cannot be used for finding the regression model.

Let us use the least squares criterion where we minimize

(9)

is called the sum of the square of the residuals.

To find  and , we minimize  with respect to  and .

(10)

(11)

giving

(12)

(13)

Noting that

(14)

(15)

Figure 3 Linear regression of vs. data showing residuals and square of residual at a typical point, .

Solving the above Equations (14) and (15) gives

(16)

(17)

Redefining

(18)

(19)

(20)

(21)

we can rewrite

(22)

(23)

# Example 1

The torque  needed to turn the torsional spring of a mousetrap through an angle,  is given below

Table 5 Torque versus angle for a torsion spring.

| Angle, Radians | Torque, |
| --- | --- |
| 0.698132 | 0.188224 |
| 0.959931 | 0.209138 |
| 1.134464 | 0.230052 |
| 1.570796 | 0.250965 |
| 1.919862 | 0.313707 |

Find the constants  and  of the regression model

# Solution

Table 6 shows the summations needed for the calculation of the constants of the regression model.

Table 6 Tabulation of data for calculation of needed summations.

| i |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 | radians |  | radians |  |
| 2 | 0.698132 | 0.188224 |  |  |
| 3 | 0.959931 | 0.209138 |  |  |
| 4 | 1.134464 | 0.230052 | 1.2870 |  |
| 5 | 1.570796 | 0.250965 | 2.4674 |  |
| 6 | 1.919862 | 0.313707 | 3.6859 |  |
|  | 6.2831 | 1.1921 | 8.8491 | 1.5896 |

N-m

Figure 4 Linear regression of torque vs. angle data

# Example 2

To find the longitudinal modulus of a composite material, the following data, as given in Table 7, is collected.

Table 7 Stress vs. strain data for a composite material.

| Strain (%) | Stress () |
| --- | --- |
| 0 | 0 |
| 0.183 | 306 |
| 0.36 | 612 |
| 0.5324 | 917 |
| 0.702 | 1223 |
| 0.867 | 1529 |
| 1.0244 | 1835 |
| 1.1774 | 2140 |
| 1.329 | 2446 |
| 1.479 | 2752 |
| 1.5 | 2767 |
| 1.56 | 2896 |

Find the longitudinal modulus  using the regression model.

(24)

# Solution

Rewriting data from Table 7, stresses versus strain data in Table 8

Table 8  Stress vs strain data for a composite in SI system of units

| Strain () | Stress () |
| --- | --- |
| 0.0000 | 0.0000 |

Applying the least square method, the residuals  at each data point is

The sum of square of the residuals is

Again, to find the constant , we need to minimize  by differentiating with respect to  and then equating to zero

From there, we obtain

(25)

The summations used in Equation (25) are given in the Table 9.

Table 9 Tabulation for Example 2 for needed summations

| 1 | 0.0000 | 0.0000 | 0.0000 | 0.0000 |
| --- | --- | --- | --- | --- |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |
| 5 |  |  |  |  |
| 6 |  |  |  |  |
| 7 |  |  |  |  |
| 8 |  |  |  |  |
| 9 |  |  |  |  |
| 10 |  |  |  |  |
| 11 |  |  |  |  |
| 12 |  |  |  |  |

Figure 5 Linear regression model of stress vs. strain for a composite material.

# Appendix

Do the values of the constants of the least squares straight-line regression model correspond to a minimum?  Is the straight line unique?

# ANSWER:

Given  data pairs,, the best fit for the straight line regression model

(A.1)

is found by the method of least squares.

Starting with the sum of the square of the residuals , we get

(A.2)

and using

(A.3)

(A.4)

gives two simultaneous linear equations whose solution is

(A.5a)

(A.5b)

But does this give the minimum of value of ?  The first derivative only tells us about a local extreme, not whether it is a minimum or a maximum.

We need to conduct a second derivative test to find out whether the point  from Equation (A.5) gives the minimum or maximum of .

What is the second derivative test for a minimum if we have a function of two variables?

If you have a function  and we found a critical point  from the first derivative test, then  is a minimum point if

, and						         (A.6)

OR 							         (A.7)

From Equation (2)

(A.8)

(A.9)

then

(A.10)

(A.11)

(A.12)

So we satisfy condition (A.7) as from Equation (A.10),  is a positive number and from Equation (A.11) is a positive number as assuming that all data points are NOT zero is reasonable.

Is the other condition for being a minimum as given by Equation (A.6) met?  Yes, we can show (the proof is not given)

(A.13)

So the values of  and  that we have in Equations (A.5a) and (A.5b), are in fact a minimum.  Also, this minimum is an absolute minimum because the first derivative is zero for only one point as given by Equations (A.5a) and (A.5b).  Hence, this also makes the straight-line regression model unique.

| LINEAR REGRESSION |  |
| --- | --- |
| Topic | Linear Regression |
| Summary | Textbook notes of Linear Regression |
| Major | Chemical Engineering |
| Authors | Egwu Kalu, Autar Kaw, Cuong Nguyen |
| Date | September 10, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

y = 6

y

x