###### Chapter 03.05

###### Secant Method of Solving Nonlinear Equations

After reading this chapter, you should be able to:

- derive the secant method to solve for the roots of a nonlinear equation,

- use the secant method to numerically solve a nonlinear equation.

# What is the secant method and why would I want to use it instead of the Newton-Raphson method?

The Newton-Raphson method of solving a nonlinear equation  is given by the iterative formula

(1)

One of the drawbacks of the Newton-Raphson method is that you have to evaluate the derivative of the function.  With availability of symbolic manipulators such as Maple, MathCAD, MATHEMATICA and MATLAB, this process has become more convenient.  However, it still can be a laborious process, and even intractable if the function is derived as part of a numerical scheme.  To overcome these drawbacks, the derivative of the function,  is approximated as

(2)

Substituting Equation (2) in Equation (1) gives

(3)

The above equation is called the secant method.  This method now requires two initial guesses, but unlike the bisection method, the two initial guesses do not need to bracket the root of the equation.  The secant method is an open method and may or may not converge.  However, when secant method converges, it will typically converge faster than the bisection method.  However, since the derivative is approximated as given by Equation (2), it typically converges slower than the Newton-Raphson method.

The secant method can also be derived from geometry, as shown in Figure 1.  Taking two initial guesses,  and , one draws a straight line between  and  passing through the -axis at .  ABE and DCE are similar triangles.

Hence

On rearranging, the secant method is given as

Figure 1 Geometrical representation of the secant method.

# Example 1

A trunnion has to be cooled before it is shrink fitted into a steel hub.

Figure 2 Trunnion to be slid through the hub after contracting.

The equation that gives the temperature  to which the trunnion has to be cooled to obtain the desired contraction is given by

Use the secant method of finding roots of equations to find the temperature  to which the trunnion has to be cooled to. Conduct three iterations to estimate the root of the above equation. Find the absolute relative approximate error at the end of each iteration and

the number of significant digits at least correct at the end of each iteration.

# Solution

Let us take the initial guesses of the root of  as   and .

## Iteration 1

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 1 is

The number of significant digits at least correct is 1, because the absolute relative approximate error is less than .

## Iteration 2

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 2 is

The number of significant digits at least correct is 3.

## Iteration 3

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 3 is

The number of significant digits at least correct is 6, because the absolute relative approximate error is less than .

| NONLINEAR EQUATIONS |  |
| --- | --- |
| Topic | Secant Method |
| Summary | Textbook notes and examples of the Secant Method |
| Major | Mechanical Engineering |
| Authors | Autar Kaw |
| Date | November 17, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

f (x)

f (xi)

f (xi–1)

xi+1

xi–1

xi

x

B

C

A

D

E