###### Chapter 08.07

###### Finite Difference Method for Ordinary Differential Equations

After reading this chapter, you should be able to

- Understand what the finite difference method is and how to use it to solve problems.

# What is the finite difference method?

The finite difference method is used to solve ordinary differential equations that have conditions imposed on the boundary rather than at the initial point.  These problems are called boundary-value problems.  In this chapter, we solve second-order ordinary differential equations of the form

, 								 (1)

with boundary conditions

and 								 (2)

Many academics refer to boundary value problems as position-dependent and initial value problems as time-dependent.  That is not necessarily the case as illustrated by the following examples.

The differential equation that governs the deflection  of a simply supported beam under uniformly distributed load (Figure 1) is given by

(3)

where

location along the beam (in)

Young’s modulus of elasticity of the beam (psi)

second moment of area (in4)

uniform loading intensity (lb/in)

length of beam (in)

The conditions imposed to solve the differential equation are

(4)

Clearly, these are boundary values and hence the problem is considered a boundary-value problem.

Figure 1 Simply supported beam with uniform distributed load.

Now consider the case of a cantilevered beam with a uniformly distributed load (Figure 2).  The differential equation that governs the deflection  of the beam is given by

(5)

where

location along the beam (in)

Young’s modulus of elasticity of the beam (psi)

second moment of area (in4)

uniform loading intensity (lb/in)

length of beam (in)

The conditions imposed to solve the differential equation are

(6)

Clearly, these are initial values and hence the problem needs to be considered as an initial value problem.

Figure 2 Cantilevered beam with a uniformly distributed load.

# Example 1

The deflection  in a simply supported beam with a uniform load and a tensile axial load is given by

(E1.1)

where

location along the beam (in)

tension applied (lbs)

Young’s modulus of elasticity of the beam (psi)

second moment of area (in4)

uniform loading intensity (lb/in)

length of beam (in)

Figure 3 Simply supported beam for Example 1.

Given,

lbs, lbs/in, , , and ,

a) Find the deflection of the beam at .  Use a step size of  and approximate the derivatives by central divided difference approximation.

b) Find the relative true error in the calculation of .

# Solution

a) Substituting the given values,

(E1.2)

Approximating the derivative  at node  by the central divided difference approximation,

Figure 4 Illustration of finite difference nodes using central divided difference method.

(E1.3)

We can rewrite the equation as

(E1.4)

Since , we have 4 nodes as given in Figure 3

Figure 5 Finite difference method from to with .

The location of the 4 nodes then is

Writing the equation at each node, we get

Node 1:  From the simply supported boundary condition at , we obtain

(E1.5)

Node 2:  Rewriting equation (E1.4) for node 2 gives

(E1.6)

Node 3:  Rewriting equation (E1.4) for node 3 gives

(E1.7)

Node 4:  From the simply supported boundary condition at , we obtain

(E1.8)

Equations (E1.5-E1.8) are 4 simultaneous equations with 4 unknowns and can be written in matrix form as

The above equations have a coefficient matrix that is tridiagonal (we can use Thomas’ algorithm to solve the equations) and is also strictly diagonally dominant (convergence is guaranteed if we use iterative methods such as the Gauss-Siedel method).  Solving the equations we get,

The exact solution of the ordinary differential equation is derived as follows.  The homogeneous part of the solution is given by solving the characteristic equation

Therefore,

The particular part of the solution is given by

Substituting the differential equation (E1.2) gives

Equating terms gives

Solving the above equation gives

The particular solution then is

The complete solution is then given by

Applying the following boundary conditions

we obtain the following system of equations

These equations are represented in matrix form by

A number of different numerical methods may be utilized to solve this system of equations such as the Gaussian elimination.  Using any of these methods yields

Substituting these values back into the equation gives

Unlike other examples in this chapter and in the book, the above expression for the deflection of the beam is displayed with a larger number of significant digits.  This is done to minimize the round-off error because the above expression involves subtraction of large numbers that are close to each other.

b) To calculate the relative true error, we must first calculate the value of the exact solution at .

The true error is given by

= Exact Value – Approximate Value

The relative true error is given by

# Example 2

Take the case of a pressure vessel that is being tested in the laboratory to check its ability to withstand pressure.  For a thick pressure vessel of inner radius  and outer radius , the differential equation for the radial displacement  of a point along the thickness is given by

(E2.3)

The inner radius  and the outer radius , and the material of the pressure vessel is ASTM A36 steel. The yield strength of this type of steel is 36 ksi. Two strain gages that are bonded tangentially at the inner and the outer radius measure normal tangential strain as

(E2.4a,b)

at the maximum needed pressure. Since the radial displacement and tangential strain are related simply by

,									       (E2.5)

then

The maximum normal stress in the pressure vessel is at the inner radius  and is given by

(E2.7)

where

Young’s modulus of steel (E= 30 Msi)

Poisson’s ratio (0.3)

The factor of safety, FS is given by

(E2.8)

- Divide the radial thickness of the pressure vessel into 6 equidistant nodes, and find the radial displacement profile

- Find the maximum normal stress and factor of safety as given by equation (E2.8)

- Find the exact value of the maximum normal stress as given by equation (E2.8) if it is given that the exact expression for radial displacement is of the form

.

Calculate the relative true error.

Solution

a)  The radial locations from  to  are divided into  equally spaced segments, and hence resulting in  nodes.  This will allow us to find the dependent variable  numerically at these nodes.

At node  along the radial thickness of the pressure vessel,

(E2.9)

(E2.10)

Such substitutions will convert the ordinary differential equation into a linear equation (but with more than one unknown).  By writing the resulting linear equation at different points at which the ordinary differential equation is valid, we get simultaneous linear equations that can be solved by using techniques such as Gaussian elimination, the Gauss-Siedel method, etc.

Substituting these approximations from Equations (E2.9) and (E2.10) in Equation (E2.3)

(E2.11)

(E2.12)

Let us break the thickness, , of the pressure vessel into  nodes, that is  is node  and  is node . That means we have  unknowns.

We can write the above equation for nodes.  This will give us  equations.  At the edge nodes,  and , we use the boundary conditions of

This gives a total of  equations. So we have  unknowns and  linear equations. These can be solved by any of the numerical methods used for solving simultaneous linear equations.

We have been asked to do the calculations for  that is a total of 6 nodes. This gives

"

At node ,   			                                         (E2.13)

At node 				                             (E2.14)

(E2.15)

At node

(E2.16)

At node

(E2.17)

At node   ″

(E2.18)

At node  ″

″					                             (E2.19)

Writing Equation (E2.13) to (E2.19) in matrix form gives

=

The above equations are a tri-diagonal system of equations and special algorithms such as Thomas’ algorithm can be used to solve such a system of equations.

″

″

″

″

″

″

b)   To find the maximum stress, it is given by Equation (E2.7) as

″

The maximum stress in the pressure vessel then is

So the factor of safety  from Equation (E2.8) is

c)  The differential equation has an exact solution and is given by the form

(E2.20)

where  and  are found by using the boundary conditions at  and .

giving

Thus

(E2.21)

(E2.22)

The true error is

The absolute relative true error is

# Example 3

The approximation in Example 2

is first order accurate, that is , the true error is of .

The approximation

(E3.1)

is second order accurate, that is , the true error is

Mixing these two approximations will result in the order of accuracy of  and , that is .

So it is better to approximate

(E3.2)

because this equation is second order accurate.  Repeat Example 2 with the more accurate approximations.

# Solution

a)  Repeating the problem with this approximation, at node in the pressure vessel,

(E3.3)

(E3.4)

Substituting Equations (E3.3) and (E3.4) in Equation (E2.3) gives

(E3.5)

At node "

" 						                               (E3.6)

At node

(E3.7)

At node  "

(E3.8)

At node  "

(E3.9)

At node   "

(E3.10)

At node  "

"					                             (E3.11)

Writing Equations (E3.6) thru (E3.11) in matrix form gives

=

The above equations are a tri-diagonal system of equations and special algorithms such as Thomas’ algorithm can be used to solve such equations.

"

"

"

"

"

"

b)

Therefore, the factor of safety  is

c)  The true error in calculating the maximum stress is

The relative true error in calculating the maximum stress is

Table 1 Comparisons of radial displacements from two methods.

| 5 | 0.0038731 | 0.0038731 | 0.0000 | 0.0038731 | 0.0000 |
| --- | --- | --- | --- | --- | --- |
| 5.6 | 0.0036110 | 0.0036165 |  | 0.0036115 |  |
| 6.2 | 0.0034152 | 0.0034222 |  | 0.0034159 |  |
| 6.8 | 0.0032683 | 0.0032743 |  | 0.0032689 |  |
| 7.4 | 0.0031583 | 0.0031618 |  | 0.0031586 |  |
| 8 | 0.0030769 | 0.0030769 | 0.0000 | 0.0030769 | 0.0000 |

| ORDINARY DIFFERENTIAL EQUATIONS |  |
| --- | --- |
| Topic | Finite Difference Methods of Solving Ordinary Differential Equations |
| Summary | Textbook notes of Finite Difference Methods of solving ordinary differential equations |
| Major | General Engineering |
| Authors | Autar Kaw, Cuong Nguyen, Luke Snyder |
| Date | July 17, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

i-1

i+1

b

a

i

0……

a

……n

b

i-1

i

Figure 4  Nodes along the radial direction.

i+1