###### Chapter 07.00C

###### Physical Problem for Integration
Civil Engineering

Problem Statement

In a class X528 well in New York State, you are asked to find if the concentration of benzene is below the toxicity level of  at a distance of  from the point of contamination.  The contamination at the source is constant at for a whole year.

# Solution

The equations governing transport of groundwater contaminant are quite complex.  They depend on several parameters such as “the molecular diffusion of the contaminant, physical and chemical isotropy of the medium, and actual direction of the groundwater flow” [1].

Here we consider that the groundwater is flowing in one-direction,  and the aquifer has isotropic and homogeneous physical and chemical characteristics.  In that case, the governing equation [2] for the concentration  of the contaminant is given by

.							                         (1)

where

= velocity of ground water flow in the -direction

= time

= distance from source

= dispersion coefficient .

To solve this partial differential equation (1) [3], we use Laplace transforms.  Applying Laplace transform to both sides on the variable ,

.							             (2)

where

Since the initial concentration is zero,

,

Equation (2) becomes

(3)

This is a homogenous ordinary differential equation.  It is linear with fixed coefficients.  The characteristics equation of the above ordinary differential equation (3) is

(4)

The homogeneous as well as the complete solution of Equation (3) is

(5)

At , that is far away from the source, the concentration of the pollutant  is zero, that is , that is, .  This forces as the exponent of the exponential term is always positive as .  The exponent of the exponential term on the second term will be negative as for all values of as .  Equation (5) hence reduces to

(6)

At , (initial concentration, ), then .  Substituting this in equation (6) gives

then equation (6) is

(7)

Let

Then Equation (7) becomes

(8)

Using the formulas

, and

then

(9)

Then from

we get

Let

,

then

(10)

Using Equation (10), Equation (8) becomes

(11)

Substituting back

,

(12)

The velocity of the ground flow,  is given by

(13)

where

= effective Darcian porosity,

= permeability,

ground water gradient.

Assuming

= 22% = 0.22

= 0.002

.

Then from Equation (13),

.

So in the formula for concentration given by Equation (12), substituting

the concentration of benzene after 1 year at a distance of is

(14)

As you can see to calculate the concentration of benzene at , we need to calculate  and .  How is  defined?

So

Since decays rapidly as , we will approximate

So to find whether the concentration of benzene is below toxicity level, we need to find the integral numerically.

# QUESTIONS

- What is the concentration of benzene after 2 years?

- After 1 year, at what distance does the concentration go below the toxicity level of 0.5 mg/L?

# REFERENCES

- EPA Region 5 Water Draft UIC Class IV and V Site Assessment Guidelines, http://www.epa.gov/R5water/uic/r5guid/siteasst.htm, last accessed July 2004.

- Fetter, C.W., Jr., Applied Hydrology, Merill Publishing Co, Columbus, 1980.

- Li, W., Differential Equations of Hydraulic Transients, Dispersion, and Groundwater Flow, Prentice Hall, Englewood Cliffs, NJ, 1972

| Topic | INTEGRATION |
| --- | --- |
| Sub Topic | Physical problem |
| Summary | Find if the concentration of benzene is above or below the toxicity limit at a critical distance from its source. |
| Authors | Autar Kaw |
| Last Revised | December 7, 2008 |
| Web Site | http://numericalmethods.eng.usf.edu |