###### Chapter 05.02

###### Direct Method of Interpolation

After reading this chapter, you should be able to:

- apply the direct method of interpolation,

- solve problems using the direct method of interpolation, and

- use the direct method interpolants to find derivatives and integrals of discrete functions.

# What is interpolation?

Many times, data is given only at discrete points such as  , , .  So, how then does one find the value of  at any other value of ?  Well, a continuous function  may be used to represent the  data values with  passing through the  points (Figure 1).  Then one can find the value of  at any other value of .  This is called interpolation.

Of course, if  falls outside the range of  for which the data is given, it is no longer interpolation but instead is called extrapolation.

So what kind of function  should one choose?  A polynomial is a common choice for an interpolating function because polynomials are easy to

evaluate,

differentiate, and

integrate

relative to other choices such as a trigonometric and exponential series.

Polynomial interpolation involves finding a polynomial of order  that passes through the  points.  One of the methods of interpolation is called the direct method.  Other methods include Newton’s divided difference polynomial method and the Lagrangian interpolation method.  We will discuss the direct method in this chapter.

Figure 1 Interpolation of discrete data.

# Direct Method

The direct method of interpolation is based on the following premise.  Given  data points, fit a polynomial of order  as given below

(1)

through the data, where  are  real constants.  Since  values of  are given at  values of , one can write  equations.  Then the  constants,  can be found by solving the  simultaneous linear equations.  To find the value of  at a given value of , simply substitute the value of  in Equation 1.

But, it is not necessary to use all the data points.  How does one then choose the order of the polynomial and what data points to use?  This concept and the direct method of interpolation are best illustrated using examples.

# Example 1

A robot arm with a rapid laser scanner is doing a quick quality check on holes drilled in a  rectangular plate. The centers of the holes in the plate describe the path the arm needs to take, and the hole centers are located on a Cartesian coordinate system (with the origin at the bottom left corner of the plate) given by the specifications in Table 1.

Table 1  The coordinates of the holes on the plate.

| (in.) | (in.) |
| --- | --- |
| 2.00 | 7.2 |
| 4.25 | 7.1 |
| 5.25 | 6.0 |
| 7.81 | 5.0 |
| 9.20 | 3.5 |
| 10.60 | 5.0 |

Figure 1 Location of holes on the rectangular plate.

If the laser is traversing from  to  in a linear path, what is the value of  at  using the direct method of interpolation and a first order polynomial?

# Solution

For first order polynomial interpolation (also called linear interpolation), we choose the value of  given by

Figure 2 Linear interpolation.

Since we want to find the value of  at , using the two points  and , then

gives

Writing the equations in matrix form, we have

Solving the above two equations gives

Hence

# Example 2

A robot arm with a rapid laser scanner is doing a quick quality check on holes drilled in a  rectangular plate. The centers of the holes in the plate describe the path the arm needs to take, and the hole centers are located on a Cartesian coordinate system (with the origin at the bottom left corner of the plate) given by the specifications in Table 2.

Table 2  The coordinates of the holes on the plate.

| (in.) | (in.) |
| --- | --- |
| 2.00 | 7.2 |
| 4.25 | 7.1 |
| 5.25 | 6.0 |
| 7.81 | 5.0 |
| 9.20 | 3.5 |
| 10.60 | 5.0 |

If the laser is traversing from  to  to  in a quadratic path, what is the value of  at using the direct method of interpolation and a second order polynomial?  Find the absolute relative approximate error for the second order polynomial approximation.

# Solution

For second order polynomial interpolation (also called quadratic interpolation), we choose the value of  given by

Figure 3 Quadratic interpolation.

Since we want to find the value of  at , using the three points as ,  and , then

gives

Writing the three equations in matrix form, we have

Solving the above three equations gives

Hence

At ,

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

# Example 3

A robot arm with a rapid laser scanner is doing a quick quality check on holes drilled in a  rectangular plate. The centers of the holes in the plate describe the path the arm needs to take, and the hole centers are located on a Cartesian coordinate system (with the origin at the bottom left corner of the plate) given by the specifications in Table 3.

Table 3  The coordinates of the holes on the plate.

| (in.) | (in.) |
| --- | --- |
| 2.00 | 7.2 |
| 4.25 | 7.1 |
| 5.25 | 6.0 |
| 7.81 | 5.0 |
| 9.20 | 3.5 |
| 10.60 | 5.0 |

Find the path traversed through the six points using the direct method of interpolation and a fifth order polynomial.

# Solution

For fifth order polynomial interpolation, also called quintic interpolation, we choose the value of  given by

Figure 4 5th order polynomial interpolation.

Using the six points,

gives

Writing the six equations in matrix form, we have

Solving the above six equations gives

Hence

Figure 5 Fifth order polynomial to traverse points of robot path (using direct method of interpolation).

| INTERPOLATION |  |
| --- | --- |
| Topic | Direct Method of Interpolation |
| Summary | Textbook notes on the direct method of interpolation. |
| Major | Computer Engineering |
| Authors | Autar Kaw, Peter Warr, Michael Keteltas |
| Date | November 9, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |