###### Chapter 05.04

###### Lagrangian Interpolation

After reading this chapter, you should be able to:

derive Lagrangian method of interpolation,

solve problems using Lagrangian method of interpolation, and

use Lagrangian interpolants to find derivatives and integrals of discrete functions.

# What is interpolation?

Many times, data is given only at discrete points such as  , , .  So, how then does one find the value of  at any other value of ?  Well, a continuous function  may be used to represent the  data values with  passing through the  points (Figure 1).  Then one can find the value of  at any other value of .  This is called interpolation.

Of course, if  falls outside the range of  for which the data is given, it is no longer interpolation but instead is called extrapolation.

So what kind of function  should one choose?  A polynomial is a common choice for an interpolating function because polynomials are easy to

evaluate,

differentiate, and

integrate,

relative to other choices such as a trigonometric and exponential series.

Polynomial interpolation involves finding a polynomial of order  that passes through the  data points.  One of the methods used to find this polynomial is called the Lagrangian method of interpolation.  Other methods include Newton’s divided difference polynomial method and the direct method.  We discuss the Lagrangian method in this chapter.

Figure 1 Interpolation of discrete data.

The Lagrangian interpolating polynomial is given by

where  in  stands for the  order polynomial that approximates the function  given at  data points as , and

is a weighting function that includes a product of  terms with terms of  omitted.  The application of Lagrangian interpolation will be clarified using an example.

# Example 1

A robot arm with a rapid laser scanner is doing a quick quality check on holes drilled in a  rectangular plate. The centers of the holes in the plate describe the path the arm needs to take, and the hole centers are located on a Cartesian coordinate system (with the origin at the bottom left corner of the plate) given by the specifications in Table 1.

Table 1  The coordinates of the holes on the plate.

| (in.) | (in.) |
| --- | --- |
| 2.00 | 7.2 |
| 4.25 | 7.1 |
| 5.25 | 6.0 |
| 7.81 | 5.0 |
| 9.20 | 3.5 |
| 10.60 | 5.0 |

Figure 2 Location of the holes on the rectangular plate.

If the laser is traversing from  to  in a linear path, what is the value of  at  using the Lagrangian method and a first order polynomial?

# Solution

For first order Lagrange polynomial interpolation (also called linear interpolation), we choose the value of  as given by

Figure 3 Linear interpolation.

Since we want to find the value of  at , using the two points  and , then

gives

Hence

You can see that  and  are like weightages given to the values of  at  and  to calculate the value of  at

# Example 2

A robot arm with a rapid laser scanner is doing a quick quality check on holes drilled in a  rectangular plate. The centers of the holes in the plate describe the path the arm needs to take, and the hole centers are located on a Cartesian coordinate system (with the origin at the bottom left corner of the plate) given by the specifications in Table 2.

Table 2  The coordinates of the holes on the plate.

| (in.) | (in.) |
| --- | --- |
| 2.00 | 7.2 |
| 4.25 | 7.1 |
| 5.25 | 6.0 |
| 7.81 | 5.0 |
| 9.20 | 3.5 |
| 10.60 | 5.0 |

If the laser is traversing from  to  to  in a quadratic path, what is the value of  at using a second order Lagrange polynomial? Find the absolute relative approximate error for the second order polynomial approximation.

# Solution

For second order Lagrange polynomial interpolation (also called quadratic interpolation), we choose the value of  given by

Figure 4 Quadratic interpolation.

Since we want to find the value of  at , using the three points as ,

and , then

gives

Hence

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

# Example 3

A robot arm with a rapid laser scanner is doing a quick quality check on holes drilled in a  rectangular plate. The centers of the holes in the plate describe the path the arm needs to take, and the hole centers are located on a Cartesian coordinate system (with the origin at the bottom left corner of the plate) given by the specifications in Table 3.

Table 3  The coordinates of the holes on the plate.

| (in.) | (in.) |
| --- | --- |
| 2.00 | 7.2 |
| 4.25 | 7.1 |
| 5.25 | 6.0 |
| 7.81 | 5.0 |
| 9.20 | 3.5 |
| 10.60 | 5.0 |

Find the path traversed through the six points using a fifth order Lagrange polynomial.

# Solution

For fifth order Lagrange polynomial interpolation (also called quintic interpolation), we choose the value of  given by

Figure 5 5th order polynomial interpolation.

Using the six points,

gives

Figure 6 Fifth order polynomial to traverse points of robot path (using Lagrangian method of interpolation).

| INTERPOLATION |  |
| --- | --- |
| Topic | Lagrange Interpolation |
| Summary | Textbook notes on the Lagrangian method of interpolation |
| Major | Computer Engineering |
| Authors | Autar Kaw, Michael Keteltas |
| Last Revised | November 11, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

(x0, y0)

(x1, y1)

f1(x)

x

y

(x0, y0)

(x1, y1)

(x2, y2)

f2(x)

x

y

y

x

f5(x)

(x0, y0)

(x1, y1)

(x2, y2)

(x3, y3)

(x4, y4)

(x5, y5)