###### Chapter 05.03

###### Newton’s Divided Difference Interpolation

After reading this chapter, you should be able to:

- derive Newton’s divided difference method of interpolation,

- apply Newton’s divided difference method of interpolation, and

- apply Newton’s divided difference method interpolants to find derivatives and integrals.

# What is interpolation?

Many times, data is given only at discrete points such as  , , .  So, how then does one find the value of  at any other value of ?  Well, a continuous function  may be used to represent the  data values with  passing through the  points (Figure 1).  Then one can find the value of  at any other value of .  This is called interpolation.

Of course, if  falls outside the range of  for which the data is given, it is no longer interpolation but instead is called extrapolation.

So what kind of function  should one choose?  A polynomial is a common choice for an interpolating function because polynomials are easy to

evaluate,

differentiate, and

integrate,

relative to other choices such as a trigonometric and exponential series.

Polynomial interpolation involves finding a polynomial of order  that passes through the  points.  One of the methods of interpolation is called Newton’s divided difference polynomial method.  Other methods include the direct method and the Lagrangian interpolation method.  We will discuss Newton’s divided difference polynomial method in this chapter.

# Newton’s Divided Difference Polynomial Method

To illustrate this method, linear and quadratic interpolation is presented first.  Then, the general form of Newton’s divided difference polynomial method is presented.  To illustrate the general form, cubic interpolation is shown in Figure 1.

Figure 1 Interpolation of discrete data.

Linear Interpolation

Given  and  fit a linear interpolant through the data.  Noting  and , assume the linear interpolant  is given by (Figure 2)

Since at ,

and at ,

giving

So

giving the linear interpolant as

Figure 2 Linear interpolation.

# Example 1

Thermistors are used to measure the temperature of bodies. Thermistors are based on materials’ change in resistance with temperature. To measure temperature, manufacturers provide you with a temperature vs. resistance calibration curve. If you measure resistance, you can find the temperature. A manufacturer of thermistors makes several observations with a thermistor, which are given in Table 1.

Table 1  Temperature as a function of resistance.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |
| --- | --- |

Figure 3 Resistance vs. temperature.

Determine the temperature corresponding to 754.8 ohms using Newton’s divided difference method of interpolation and a first order polynomial.

# Solution

For linear interpolation, the temperature is given by

Since we want to find the temperature at  and we are using a first order polynomial, we need to choose the two data points that are closest to  that also bracket  to evaluate it. The two points are  and .

Then

gives

Hence

At

If we expand

we get

This is the same expression that was obtained with the direct method.

Figure 4 Quadratic interpolation.

# Example 2

Thermistors are used to measure the temperature of bodies. Thermistors are based on materials’ change in resistance with temperature. To measure temperature, manufacturers provide you with a temperature vs. resistance calibration curve. If you measure resistance, you can find the temperature. A manufacturer of thermistors makes several observations with a thermistor, which are given in Table 2.

Table 2  Temperature as a function of resistance.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |
| --- | --- |

Determine the temperature corresponding to 754.8 ohms using Newton’s divided difference method of interpolation and a second order polynomial. Find the absolute relative approximate error for the second order polynomial approximation.

# Solution

For quadratic interpolation, the temperature is given by

Since we want to find the temperature at  and we are using a second order polynomial, we need to choose the three data points that are closest to  that also bracket  to evaluate it. The three points are   and .

Then

gives

Hence

At

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

If we expand,

we get

This is the same expression that was obtained with the direct method.

# General Form of Newton’s Divided Difference Polynomial

In the two previous cases, we found linear and quadratic interpolants for Newton’s divided difference method.  Let us revisit the quadratic polynomial interpolant formula

where

Note that  and  are finite divided differences. and  are the first, second, and third finite divided differences, respectively.  We denote the first divided difference by

the second divided difference by

and the third divided difference by

where  and  are called bracketed functions of their variables enclosed in square brackets.

Rewriting,

This leads us to writing the general form of the Newton’s divided difference polynomial for  data points, , as

where

where the definition of the  divided difference is

From the above definition, it can be seen that the divided differences are calculated recursively.

For an example of a third order polynomial, given    and

Figure 5 Table of divided differences for a cubic polynomial.

# Example 3

Thermistors are used to measure the temperature of bodies. Thermistors are based on materials’ change in resistance with temperature. To measure temperature, manufacturers provide you with a temperature vs. resistance calibration curve. If you measure resistance, you can find the temperature. A manufacturer of thermistors makes several observations with a thermistor, which are given in Table 3.

Table 3  Temperature as a function of resistance.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |
| --- | --- |

- Determine the temperature corresponding to 754.8 ohms using Newton’s divided difference method of interpolation and a third order polynomial. Find the absolute relative approximate error for the third order polynomial approximation.

- The actual calibration curve used by industry is given by

substituting  and

the calibration curve is given by

Table 4  Manipulation for the given data.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 | 7.0040 6.8149 6.4552 6.1117 | 0.039820 0.033188 0.024925 0.019949 |
| --- | --- | --- | --- |

Find the calibration curve and find the temperature corresponding to 754.8 ohms. What is the difference between the results from part (a)? Is the difference larger using results from part (a) or part (b), if the actual measured value at 754.8 ohms is ?

# Solution

a) For cubic interpolation, the temperature is given by

Since we want to find the temperature at  we need to choose the four data points that are closest to  that also bracket  to evaluate it. The four data points are    and .

Then

gives

Hence

At

The absolute relative approximate error  obtained between the results from the second and third order polynomial is

If we expand

we get

This is the same expression that was obtained with the direct method.

b) Finding the cubic interpolant using Newton’s divided difference for

requires that we first calculate the new values of  and .

| 7.0040 6.8149 6.4552 6.1117 | 0.039820 0.033188 0.024925 0.019949 |
| --- | --- |

Then

gives

Hence

Since we’re looking for the temperature at , we will be using

At

Finally, since

Since the actual measured value at 754.8 ohms is  the absolute relative true error for the value found in part (a) is

and for part (b) is

Therefore, the cubic polynomial interpolant given by Newton’s divided difference method, that is,

obtained more accurate results than the calibration curve of

| INTERPOLATION |  |
| --- | --- |
| Topic | Newton’s Divided Difference Interpolation |
| Summary | Examples of Newton’s divided difference interpolation. |
| Major | Electrical Engineering |
| Authors | Autar Kaw |
| Date | November 14, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |