###### Chapter 01.04

###### Binary Representation of Numbers

After reading this chapter, you should be able to:

- convert a base-10 real number to its binary representation,

- convert a binary number to an equivalent base-10 number.

In everyday life, we use a number system with a base of 10.  For example, look at the number 257.56.  Each digit in 257.56 has a value of 0 through 9 and has a place value.  It can be written as

In a binary system, we have a similar system where the base is made of only two digits 0 and 1. So it is a base 2 system.  A number like (1011.0011) in base-2 represents the decimal number as

in the decimal system.

To understand the binary system, we need to be able to convert binary numbers to decimal numbers and vice-versa.

We have already seen an example of how binary numbers are converted to decimal numbers. Let us see how we can convert a decimal number to a binary number. For example take the decimal number 11.1875.  First, look at the integer part: 11.

  - Divide 11 by 2.  This gives a quotient of 5 and a remainder of 1.  Since the remainder is 1, .

  - Divide the quotient 5 by 2.  This gives a quotient of 2 and a remainder of 1.  Since the remainder is 1, .

  - Divide the quotient 2 by 2.  This gives a quotient of 1 and a remainder of 0.  Since the remainder is 0, .

  - Divide the quotient 1 by 2.  This gives a quotient of 0 and a remainder of 1.  Since the remainder is , .

Since the quotient now is 0, the process is stopped.  The above steps are summarized in Table 1.

Table 1   Converting a base-10 integer to binary representation.

|  | Quotient | Remainder |
| --- | --- | --- |
| 11/2 | 5 |  |
| 5/2 | 2 |  |
| 2/2 | 1 |  |
| 1/2 | 0 |  |

Hence

For any integer, the algorithm for finding the binary equivalent is given in the flow chart on the next page.

Now let us look at the decimal part, that is, 0.1875.

- Multiply 0.1875 by 2.  This gives 0.375.  The number before the decimal is 0 and the number after the decimal is 0.375.  Since the number before the decimal is 0, .

- Multiply the number after the decimal, that is, 0.375 by 2.  This gives 0.75.  The number before the decimal is 0 and the number after the decimal is 0.75.  Since the number before the decimal is 0, .

- Multiply the number after the decimal, that is, 0.75 by 2.  This gives 1.5.  The number before the decimal is 1 and the number after the decimal is 0.5.  Since the number before the decimal is 1, .

- Multiply the number after the decimal, that is, 0.5 by 2.  This gives 1.0.  The number before the decimal is 1 and the number after the decimal is 0.  Since the number before the decimal is 1, .

Since the number after the decimal is 0, the conversion is complete.  The above steps are summarized in Table 2.

Table 2.  Converting a base-10 fraction to binary representation.

|  | Number | Number after decimal | Number before decimal |
| --- | --- | --- | --- |
| 0.18752 | 0.375 | 0.375 |  |
| 0.3752 | 0.75 | 0.75 |  |
| 0.752 | 1.5 | 0.5 |  |
| 0.52 | 1.0 | 0.0 |  |

Hence

The algorithm for any fraction is given in a flowchart on the next page.

Having calculated

and

,

we have

.

In the above example, when we were converting the fractional part of the number, we were left with 0 after the decimal number and used that as a place to stop.  In many cases, we are never left with a 0 after the decimal number.  For example, finding the binary equivalent of 0.3 is summarized in Table 3.

Table 3.  Converting a base-10 fraction to approximate binary representation.

|  | Number | Number after decimal | Number before decimal |
| --- | --- | --- | --- |
| 0.32 | 0.6 | 0.6 |  |
| 0.62 | 1.2 | 0.2 |  |
| 0.22 | 0.4 | 0.4 |  |
| 0.42 | 0.8 | 0.8 |  |
| 0.82 | 1.6 | 0.6 |  |

As you can see the process will never end. In this case, the number can only be approximated in binary format, that is,

Q: But what is the mathematics behinds this process of converting a decimal number to binary format?

A: Let  be the decimal number written as

where

is the integer part and  is the fractional part.

We want to find the binary equivalent of .  So we can write

If we can now find in the above equation then

We now want to find the binary equivalent of .  So we can write

If we can now find in the above equation then

Let us look at this using the same example as before.

# Example 1

Convert  to base 2.

# Solution

To convert  to base 2, what is the highest power of 2 that is part of 11.  That power is 3, as  to give

What is the highest power of 2 that is part of 3.  That power is 1, as  to give

So

What is the highest power of 2 that is part of 1.  That power is 0, as  to give

Hence

To convert  to the base 2, we proceed as follows.  What is the smallest negative power of 2 that is less than or equal to 0.1875.  That power is  as .

So

What is the next smallest negative power of 2 that is less than or equal to 0.0625.  That power is  as .

So

Hence

Since

and

we get

Can you show this algebraically for any general number?

# Example 2

Convert  to base 2.

# Solution

For , conversion to binary format is shown in Table 4.

Table 4.  Conversion of base-10 integer to binary format.

|  | Quotient | Remainder |
| --- | --- | --- |
| 13/2 | 6 |  |
| 6/2 | 3 |  |
| 3/2 | 1 |  |
| 1/2 | 0 |  |

So

.

Conversion of  to binary format is shown in Table 5.

Table 5.  Converting a base-10 fraction to binary representation.

|  | Number | Number after decimal | Number before decimal |
| --- | --- | --- | --- |
| 0.8752 | 1.75 | 0.75 |  |
| 0.752 | 1.5 | 0.5 |  |
| 0.52 | 1.0 | 0.0 |  |

So

Hence

| INTRODUCTION TO NUMERICAL METHODS |  |
| --- | --- |
| Topic | Binary representation of number |
| Summary | Textbook notes on binary representation of numbers |
| Major | General Engineering |
| Authors | Autar Kaw |
| Date | September 4, 2014 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

Start

Input (N)10

i = 0

Divide N by 2 to get quotient Q & remainder R

ai = R

Is Q = 0?

n = i

(N)10 = (an. . .a0)2

STOP

Integer N to be converted to binary format

i = i+1

No

Yes

Start

Input (F)10

Multiply F by 2 to get number before decimal, S and after decimal, T

ai = S

Is T = 0?

n = i

(F)10 = (a-1. . .a-n)2

STOP

Fraction F to be converted to binary format

No

Yes