###### Chapter 03.06

###### False-Position Method of Solving a Nonlinear Equation

After reading this chapter, you should be able to

- follow the algorithm of the false-position method of solving a nonlinear equation,

- apply the false-position method to find roots of a nonlinear equation.

# Introduction

In Chapter 03.03, the bisection method was described as one of the simple bracketing methods of solving a nonlinear equation of the general form

(1)

Figure 1 False-Position Method

The above nonlinear equation can be stated as finding the value of x such that Equation (1) is satisfied.

In the bisection method, we identify proper values of  (lower bound value) and  (upper bound value) for the current bracket, such that

.                                                                                                     (2)

The next predicted/improved root  can be computed as the midpoint between  and  as

(3)

The new upper and lower bounds are then established, and the procedure is repeated until the convergence is achieved (such that the new lower and upper bounds are sufficiently close to each other).

However, in the example shown in Figure 1, the bisection method may not be efficient because it does not take into consideration that  is much closer to the zero of the function  as compared to . In other words, the next predicted root  would be closer to  (in the example as shown in Figure 1), than the mid-point between  and  .  The false-position method takes advantage of this observation mathematically by drawing a secant from the function value at  to the function value at , and estimates the root as where it crosses the x-axis.

# False-Position Method

Based on two similar triangles, shown in Figure 1, one gets

(4)

From Equation (4), one obtains

The above equation can be solved to obtain the next predicted root as

(5)

The above equation, through simple algebraic manipulations, can also be expressed as

(6)

or

(7)

Observe the resemblance of Equations (6) and (7) to the secant method.

# False-Position Algorithm

The steps to apply the false-position method to find the root of the equation are as follows.

1. Choose and  as two guesses for the root such that, or in other words,  changes sign between  and.

2. Estimate the root,  of the equation as

3. Now check the following

If, then the root lies between  and; then  and .

If, then the root lies between  and; then  and .

If, then the root is.  Stop the algorithm.

4. Find the new estimate of the root

Find the absolute relative approximate error as

where

= estimated root from present iteration

= estimated root from previous iteration

5. Compare the absolute relative approximate error with the pre-specified relative error tolerance. If, then go to step 3, else stop the algorithm. Note one should also check whether the number of iterations is more than the maximum number of iterations allowed. If so, one needs to terminate the algorithm and notify the user about it.

Note that the false-position and bisection algorithms are quite similar. The only difference is the formula used to calculate the new estimate of the root as shown in steps #2 and #4!

# Example 1

You are working for “DOWN THE TOILET COMPANY” that makes floats for ABC commodes. The floating ball has a specific gravity of 0.6 and has a radius of 5.5cm. You are asked to find the depth to which the ball is submerged when floating in water.  The equation that gives the depth  to which the ball is submerged under water is given by

Use the false-position method of finding roots of equations to find the depth  to which the ball is submerged under water. Conduct three iterations to estimate the root of the above equation. Find the absolute relative approximate error at the end of each iteration, and the number of significant digits at least correct at the end of third iteration.

Figure 2 Floating ball problem.

# Solution

From the physics of the problem, the ball would be submerged between  and,

where

that is

Let us assume

Check if the function changes sign between  and

Hence

Therefore, there is at least one root between  and, that is between 0 and 0.11.

Iteration 1

The estimate of the root is

Hence, the root is bracketed between  and, that is, between 0 and 0.0660. So, the lower and upper limits of the new bracket are , respectively.

Iteration 2

The estimate of the root is

The absolute relative approximate error for this iteration is

Hence, the lower and upper limits of the new bracket are , respectively.

Iteration 3

The estimate of the root is

The absolute relative approximate error for this iteration is

Hence, the lower and upper limits of the new bracket are

All iterations results are summarized in Table 1.  To find how many significant digits are at least correct in the last iterative value

The number of significant digits at least correct in the estimated root of 0.0624 at the end of 3rd iteration is 1.

Table 1 Root of for false-position method.

| Iteration |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 1 | 0.0000 | 0.1100 | 0.0660 | ---- |  |
| 2 | 0.0000 | 0.0660 | 0.0611 | 8.00 |  |
| 3 | 0.0611 | 0.0660 | 0.0624 | 2.05 |  |

# Example 2

Find the root of , using the initial guesses of  and and a pre-specified tolerance of .

# Solution

The individual iterations are not shown for this example, but the results are summarized in Table 2.  It takes five iterations to meet the pre-specified tolerance.

Table 2 Root of for false-position method.

| Iteration |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | -2.5 | -1 | -21.13 | 25.00 | -1.813 | N/A | 6.319 |
| 2 | -2.5 | -1.813 | -21.13 | 6.319 | -1.971 | 8.024 | 1.028 |
| 3 | -2.5 | -1.971 | -21.13 | 1.028 | -1.996 | 1.229 | 0.1542 |
| 4 | -2.5 | -1.996 | -21.13 | 0.1542 | -1.999 | 0.1828 | 0.02286 |
| 5 | -2.5 | -1.999 | -21.13 | 0.02286 | -2.000 | 0.02706 | 0.003383 |

To find how many significant digits are at least correct in the last iterative answer,

Hence, at least 3 significant digits can be trusted to be accurate at the end of the fifth iteration.

| FALSE-POSITION METHOD OF SOLVING A NONLINEAR EQUATION |
| --- |
| Topic | False-Position Method of Solving a Nonlinear Equation |
| Summary | Textbook Chapter of False-Position Method |
| Major | General Engineering |
| Authors | Duc Nguyen |
| Date | September 4, 2012 |