###### Chapter 11.00E

###### Physical Problem for Fast Fourier Transform

###### Industrial Engineering

# Problem Statement

Forecasting is a very important tool we use in daily life. We forecast traffic or length of the line at the local coffee shop based on the time of day. Figure 1 below shows monthly net electricity power generation (Billion Kilowatt-hours) for years 1973, 83, 93 and 2003. This time series exhibits interesting properties as it has both an upward trend but also seasonal behavior. Therefore, traditional methods used for forecasting stationary time series (moving averages and exponential smoothing), trend based methods (regression), or methods used for seasonal series would introduce significant errors if used for forecasting the net electricity power generation for year 2023.

Figure 1 Net electricity power generation.

Forecasting also plays a key role in the operations of firms. For example demand forecasts are used in capacity planning, inventory control and raw material procurement. Although a certain portion of future demand is random and unpredictable, other portions may exhibit trends, cycles and seasonal variations which may help forecast values reasonably close to the actual demand values.

# Modeling Seasonal Demand

Seasonal demand is characterized by a pattern that repeats every  periods. Figure 2 shows a typical seasonal demand pattern where the length of a season is shown with . Most seasonal demand forecasting models require that  is specified a priori. The most common method of seasonal forecasting is to use seasonal multipliers where the multiplier represents the difference from the average demand. For example a multiplier of 0.5 in a period means that the demand in that particular period is half of the average demand over the  period season.

Figure 2 Typical seasonal demand pattern.

Trigonometric models of Fourier transforms can also be used to forecast demand for products which exhibit periodicity. Snow tires, antifreeze and air conditioners are examples of such products. Consider the data in Table 1 where the sale of a retail outlet for 3 styles of clothing ,  and  between May 4th and April 7th is shown. The same data is plotted in Figure 3 to better visualize the demand behavior which shows a periodic change.

Table 1 Sales of a retail outlet.

|  | 2004/05 | 2004/06 | 2004/07 | 2004/08 | 2004/09 | 2004/10 | 2004/11 | 2004/12 | 2005/01 | 2005/02 | 2005/03 | 2005/04 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | 2112 | 2952 | 2831 | 4095 | 5118 | 4848 | 4931 | 7437 | 3451 | 4286 | 5107 | 3990 |
| B | 9410 | 9939 | 7327 | 9354 | 12760 | 13331 | 13913 | 20031 | 9238 | 11402 | 13673 | 10469 |
| C | 2272 | 3136 | 2814 | 4040 | 5331 | 5395 | 5547 | 7795 | 3932 | 4548 | 5319 | 3877 |

|  | 2005/05 | 2005/06 | 2005/07 | 2005/08 | 2005/09 | 2005/10 | 2005/11 | 2005/12 | 2006/01 | 2006/02 | 2006/03 | 2006/04 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | 4058 | 4373 | 3403 | 3944 | 5432 | 5488 | 5894 | 8761 | 3733 | 3934 | 5102 | 3549 |
| B | 10203 | 10681 | 7466 | 9019 | 12910 | 14003 | 14761 | 21419 | 10327 | 11524 | 14034 | 10044 |
| C | 3947 | 4075 | 3064 | 3930 | 5195 | 5526 | 5873 | 8308 | 4132 | 4539 | 5647 | 3939 |

|  | 2006/05 | 2006/06 | 2006/07 | 2006/08 | 2006/09 | 2006/10 | 2006/11 | 2006/12 | 2007/01 | 2007/02 | 2007/03 | 2007/04 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | 3507 | 4329 | 3352 | 4110 | 4959 | 4537 | 4938 | 7295 | 3149 | 3458 | 3899 | 2974 |
| B | 9801 | 10137 | 7087 | 8567 | 12072 | 11824 | 12633 | 19097 | 9098 | 10346 | 11387 | 8707 |
| C | 3733 | 4667 | 3411 | 4234 | 5598 | 5270 | 5218 | 7715 | 3833 | 3931 | 4382 | 3437 |

Figure 3 Plot of the sales data in Table 2

The shape of the data suggests the use of a function of the form

(1)

where  is the origin of the sine wave,  is the amplitude and is the angular frequency. For the above problem, the seasonal cycle repeats every 12 months, therefore Equation (1) can be stated as

The sum of square of errors the can be written as

.							 (2)

Taking the partial derivatives of Equation (2) with respect to and  respectively, we obtain the following equations.

(3)

(4)

The parameters  and  can now be determined by solving Equations (3) and (4) simultaneously.

# Questions

- Using the values for style A between 2004/05 and 2006/04, forecast the sales values for 2006/05 to 2007/04.

- Solve Question 1 for Styles B and C.

- What are your significant sources of error when your forecasts are compared with the actual sales figures?

| Topic | FAST FOURIER TRANSFORM |
| --- | --- |
| Sub Topic | Physical Problem |
| Summary | Seasonal Demand Forecasting |
| Authors | Ali Yalcin |
| Last Revised | August 16, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

N

N

25

23

21

19

17

15

13

11

9

7

5

3

1

10000

9000

8000

7000

6000

5000

4000

3000

2000

1000

0