###### Chapter 05.02

###### Direct Method of Interpolation

After reading this chapter, you should be able to:

- apply the direct method of interpolation,

- solve problems using the direct method of interpolation, and

- use the direct method interpolants to find derivatives and integrals of discrete functions.

# What is interpolation?

Many times, data is given only at discrete points such as  , , .  So, how then does one find the value of  at any other value of ?  Well, a continuous function  may be used to represent the  data values with  passing through the  points (Figure 1).  Then one can find the value of  at any other value of .  This is called interpolation.

Of course, if  falls outside the range of  for which the data is given, it is no longer interpolation but instead is called extrapolation.

So what kind of function  should one choose?  A polynomial is a common choice for an interpolating function because polynomials are easy to

evaluate,

differentiate, and

integrate

relative to other choices such as a trigonometric and exponential series.

Polynomial interpolation involves finding a polynomial of order  that passes through the  points.  One of the methods of interpolation is called the direct method.  Other methods include Newton’s divided difference polynomial method and the Lagrangian interpolation method.  We will discuss the direct method in this chapter.

Figure 1 Interpolation of discrete data.

# Direct Method

The direct method of interpolation is based on the following premise.  Given  data points, fit a polynomial of order  as given below

(1)

through the data, where  are  real constants.  Since  values of  are given at  values of , one can write  equations.  Then the  constants,  can be found by solving the  simultaneous linear equations.  To find the value of  at a given value of , simply substitute the value of  in Equation 1.

But, it is not necessary to use all the data points.  How does one then choose the order of the polynomial and what data points to use?  This concept and the direct method of interpolation are best illustrated using examples.

# Example 1

For the purpose of shrinking a trunnion into a hub, the reduction of diameter  of a trunnion shaft by cooling it through a temperature change of  is given by

where

original diameter

coefficient of thermal expansion at average temperature

The trunnion is cooled from  to , giving the average temperature as .  The table of the coefficient of thermal expansion vs. temperature data is given in Table 1.

Table 1  Thermal expansion coefficient as a function of temperature.

| Temperature, | Thermal Expansion Coefficient, |
| --- | --- |
| 80 | 6.47 |
| 0 | 6.00 |
| –60 | 5.58 |
| –160 | 4.72 |
| –260 | 3.58 |
| –340 | 2.45 |

Figure 2 Thermal expansion coefficient vs. temperature.

If the coefficient of thermal expansion needs to be calculated at the average temperature of , determine the value of the coefficient of thermal expansion at  using the direct method of interpolation and a first order polynomial.

# Solution

For first order polynomial interpolation (also called linear interpolation), we choose the coefficient of thermal expansion given by

Figure 3 Linear interpolation.

Since we want to find the coefficient of thermal expansion at , and we are using a first order polynomial, we need to choose the two data points that are closest to   that also bracket  to evaluate it. The two points are  and .

Then

gives

Writing the equations in matrix form, we have

Solving the above two equations gives

Hence

At

# Example 2

For the purpose of shrinking a trunnion into a hub, the reduction of diameter  of a trunnion shaft by cooling it through a temperature change of  is given by

where

original diameter

coefficient of thermal expansion at average temperature

The trunnion is cooled from  to , giving the average temperature as .  The table of the coefficient of thermal expansion vs. temperature data is given in Table 2.

Table 2  Thermal expansion coefficient as a function of temperature.

| Temperature, | Thermal Expansion Coefficient, |
| --- | --- |
| 80 | 6.47 |
| 0 | 6.00 |
| –60 | 5.58 |
| –160 | 4.72 |
| –260 | 3.58 |
| –340 | 2.45 |

If the coefficient of thermal expansion needs to be calculated at the average temperature of , determine the value of the coefficient of thermal expansion at  using the direct method of interpolation and a first order polynomial.

# Solution

For second order polynomial interpolation (also called quadratic interpolation), we choose the coefficient of thermal expansion given by

Figure 4 Quadratic interpolation.

Since we want to find the coefficient of thermal expansion at , and we are using a second order polynomial, we need to choose the three data points that are closest to  that also bracket  to evaluate it. These three points are ,  and .

Then

gives

Writing the three equations in matrix form, we have

Solving the above three equations gives

Hence

At

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

# Example 3

For the purpose of shrinking a trunnion into a hub, the reduction of diameter  of a trunnion shaft by cooling it through a temperature change of  is given by

where

original diameter

coefficient of thermal expansion at average temperature

The trunnion is cooled from  to , giving the average temperature as .  The table of the coefficient of thermal expansion vs. temperature data is given in Table 3.

Table 3  Thermal expansion coefficient as a function of temperature.

| Temperature, | Thermal Expansion Coefficient, |
| --- | --- |
| 80 | 6.47 |
| 0 | 6.00 |
| –60 | 5.58 |
| –160 | 4.72 |
| –260 | 3.58 |
| –340 | 2.45 |

- If the coefficient of thermal expansion needs to be calculated at the average temperature of , determine the value of the coefficient of thermal expansion at  using the direct method of interpolation and a first order polynomial. Find the absolute relative approximate error for the third order polynomial approximation.

- The actual reduction in diameter is given by

where    room temperature

temperature of cooling medium

Since

Find out the percentage difference in the reduction in the diameter by the above integral formula and the result using the thermal expansion coefficient from part (a).

# Solution

a) For third order polynomial interpolation (also called cubic interpolation), we choose the coefficient of thermal expansion given by

Figure 5 Cubic interpolation.

Since we want to find the coefficient of thermal expansion at , and we are using a third order polynomial, we need to choose the four data points closest to  that also bracket  to evaluate it. Then the four points are , ,  and .

gives

Writing the four equations in matrix form, we have

Solving the above four equations gives

Hence

The absolute relative approximate error  obtained between the results from the second and third order polynomial is

b) In finding the percentage difference in the reduction in diameter, we can rearrange the integral formula to

and since we know from part (a) that

we see that we can use the integral formula in the range from  to

Therefore,

So  using the actual reduction in diameter integral formula. If we use the average value for the coefficient of thermal expansion from part (a), we get

and  using the average value of the coefficient of thermal expansion using a third order polynomial. Considering the integral to be the more accurate calculation, the percentage difference would be

| INTERPOLATION |  |
| --- | --- |
| Topic | Direct Method of Interpolation |
| Summary | Textbook notes and examples of the direct method of interpolation. |
| Major | Mechanical Engineering |
| Authors | Autar Kaw |
| Date | November 17, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |