###### Chapter 05.04

###### Lagrangian Interpolation

After reading this chapter, you should be able to:

derive Lagrangian method of interpolation,

solve problems using Lagrangian method of interpolation, and

use Lagrangian interpolants to find derivatives and integrals of discrete functions.

# What is interpolation?

Many times, data is given only at discrete points such as  , , .  So, how then does one find the value of  at any other value of ?  Well, a continuous function  may be used to represent the  data values with  passing through the  points (Figure 1).  Then one can find the value of  at any other value of .  This is called interpolation.

Of course, if  falls outside the range of  for which the data is given, it is no longer interpolation but instead is called extrapolation.

So what kind of function  should one choose?  A polynomial is a common choice for an interpolating function because polynomials are easy to

evaluate,

differentiate, and

integrate,

relative to other choices such as a trigonometric and exponential series.

Polynomial interpolation involves finding a polynomial of order  that passes through the  data points.  One of the methods used to find this polynomial is called the Lagrangian method of interpolation.  Other methods include Newton’s divided difference polynomial method and the direct method.  We discuss the Lagrangian method in this chapter.

Figure 1 Interpolation of discrete data.

The Lagrangian interpolating polynomial is given by

where  in  stands for the  order polynomial that approximates the function  given at  data points as , and

is a weighting function that includes a product of  terms with terms of  omitted.  The application of Lagrangian interpolation will be clarified using an example.

# Example 1

To find how much heat is required to bring a kettle of water to its boiling point, you are asked to calculate the specific heat of water at . The specific heat of water is given as a  function of time in Table 1.

Table 1  Specific heat of water as a function of temperature.

| Temperature, | Specific heat, |
| --- | --- |
| 22 42 52 82 100 | 4181 4179 4186 4199 4217 |

Figure 2 Specific heat of water vs. temperature.

Determine the value of the specific heat at  using a first order Lagrange polynomial.

# Solution

For first order Lagrange polynomial interpolation (also called linear interpolation), the specific heat is given by

Figure 3 Linear interpolation.

Since we want the velocity at , we need to choose the two data points that are closest to  that also bracket  to evaluate it. The two points are  and .

Then

gives

Hence

You can see that  and  are like weightages given to the specific heats at  and  to calculate the specific heat at .

# Example 2

To find how much heat is required to bring a kettle of water to its boiling point, you are asked to calculate the specific heat of water at . The specific heat of water is given as a  function of time in Table 2.

Table 2  Specific heat of water as a function of temperature.

| Temperature, | Specific heat, |
| --- | --- |
| 22 42 52 82 100 | 4181 4179 4186 4199 4217 |

Determine the value of the specific heat at  using a second order Lagrange polynomial. Find the absolute relative approximate error for the second order polynomial approximation.

Solution

For second order Lagrange polynomial interpolation (also called quadratic interpolation), the specific heat given by

Figure 4 Quadratic interpolation.

Since we want to find the specific heat at , we need to choose the three data points that are closest to  that also bracket  to evaluate it. The three points are   and .

Then

gives

Hence

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

# Example 3

To find how much heat is required to bring a kettle of water to its boiling point, you are asked to calculate the specific heat of water at . The specific heat of water is given as a function of time in Table 3.

Table 3  Specific heat of water as a function of temperature.

| Temperature, | Specific heat, |
| --- | --- |
| 22 42 52 82 100 | 4181 4179 4186 4199 4217 |

Determine the value of the specific heat at  using a third order Lagrange polynomial. Find the absolute relative approximate error for the third order polynomial approximation.

# Solution

For third order Lagrange polynomial interpolation (also called cubic interpolation), we choose the specific heat given by

Figure 5 Cubic interpolation.

Since we wish to find the velocity at , we need to choose four data points that are closest to  and bracket  to evaluate it. The four data points are    and . (Choosing the four points as , ,  and  is equally valid.)

Then

gives

Hence

The absolute relative approximate error  obtained between the results from the second and third order polynomial is

| INTERPOLATION |  |
| --- | --- |
| Topic | Lagrange Interpolation |
| Summary | Textbook notes on the Lagrangian method of interpolation |
| Major | Chemical Engineering |
| Authors | Autar Kaw, Michael Keteltas |
| Last Revised | November 8, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

(x0, y0)

(x1, y1)

f1(x)

x

y

(x0, y0)

(x1, y1)

(x2, y2)

f2(x)

x

y

y

x

f3(x)

(x0, y0)

(x1, y1)

(x2, y2)

(x3, y3)