###### Chapter 03.04

###### Newton-Raphson Method of Solving a Nonlinear Equation

After reading this chapter, you should be able to:

- derive the Newton-Raphson method formula,

- develop the algorithm of the Newton-Raphson method,

- use the Newton-Raphson method to solve a nonlinear equation, and

- discuss the drawbacks of the Newton-Raphson method.

# Introduction

Methods such as the bisection method and the false position method of finding roots of a nonlinear equation  require bracketing of the root by two guesses.  Such methods are called bracketing methods.  These methods are always convergent since they are based on reducing the interval between the two guesses so as to zero in on the root of the equation.

In the Newton-Raphson method, the root is not bracketed.  In fact, only one initial guess of the root is needed to get the iterative process started to find the root of an equation.  The method hence falls in the category of open methods.  Convergence in open methods is not guaranteed but if the method does converge, it does so much faster than the bracketing methods.

# Derivation

The Newton-Raphson method is based on the principle that if the initial guess of the root of  is at , then if one draws the tangent to the curve at , the point  where the tangent crosses the -axis is an improved estimate of the root (Figure 1).

Using the definition of the slope of a function, at

,

which gives

(1)

Equation (1) is called the Newton-Raphson formula for solving nonlinear equations of the form .  So starting with an initial guess, , one can find the next guess, , by using Equation (1).  One can repeat this process until one finds the root within a desirable tolerance.

# Algorithm

The steps of the Newton-Raphson method to find the root of an equation   are

- Evaluate  symbolically

- Use an initial guess of the root, , to estimate the new value of the root, , as

- Find the absolute relative approximate error  as

- Compare the absolute relative approximate error with the pre-specified relative error tolerance, .  If >, then go to Step 2, else stop the algorithm.  Also, check if the number of iterations has exceeded the maximum number of iterations allowed.  If so, one needs to terminate the algorithm and notify the user.

Figure 1 Geometrical illustration of the Newton-Raphson method.

# Example 1

You are making a bookshelf to carry books that range from 8½" to 11" in height and would take up 29"of space along the length. The material is wood having a Young’s Modulus of , thickness of 3/8" and a width of 12". You want to find the maximum vertical deflection of the bookshelf. The vertical deflection of the shelf is given by

where  is the position along the length of the beam. Hence to find the maximum deflection we need to find where  and conduct the second derivative test.

Figure 2 A loaded bookshelf.

The equation that gives the position  where the deflection is maximum is given by

Use the Newton-Rapshon method of finding roots of equations to find the position  where the deflection is maximum. Conduct three iterations to estimate the root of the above equation. Find the absolute relative approximate error at the end of each iteration, and the number of significant digits at least correct at the end of each iteration.

# Solution

Let us take the initial guess of the root of  as

## Iteration 1

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 1 is

The number of significant digits at least correct is 0, as you need an absolute relative approximate error of less than  for one significant digit to be correct in your result.

## Iteration 2

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 2 is

The number of significant digits at least correct is 1, because the absolute relative approximate error is less than .

## Iteration 3

The estimate of the root is

The absolute relative approximate error  at the end of Iteration 3 is

Hence the number of significant digits at least correct is given by the largest value of  for which

So

The number of significant digits at least correct in the estimated root 14.572 is 6.

# Drawbacks of the Newton-Raphson Method

1. Divergence at inflection points

If the selection of the initial guess or an iterated value of the root turns out to be close to the inflection point (see the definition in the appendix of this chapter) of the function  in the equation , Newton-Raphson method may start diverging away from the root.  It may then start converging back to the root.  For example, to find the root of the equation

the Newton-Raphson method reduces to

Starting with an initial guess of , Table 1 shows the iterated values of the root of the equation.  As you can observe, the root starts to diverge at Iteration 6 because the previous estimate of 0.92589 is close to the inflection point of  (the value of  is zero at the inflection point). Eventually, after 12 more iterations the root converges to the exact value of .

Table 1   Divergence near inflection point.

| Iteration Number |  |
| --- | --- |
| 0 | 5.0000 |
| 1 | 3.6560 |
| 2 | 2.7465 |
| 3 | 2.1084 |
| 4 | 1.6000 |
| 5 | 0.92589 |
| 6 | –30.119 |
| 7 | –19.746 |
| 8 | –12.831 |
| 9 | –8.2217 |
| 10 | –5.1498 |
| 11 | –3.1044 |
| 12 | –1.7464 |
| 13 | –0.85356 |
| 14 | –0.28538 |
| 15 | 0.039784 |
| 16 | 0.17475 |
| 17 | 0.19924 |
| 18 | 0.2 |

Figure 3   Divergence at inflection point for .

2. Division by zero

For the equation

the Newton-Raphson method reduces to

For  or , division by zero occurs (Figure 4).  For an initial guess close to 0.02 such as , one may avoid division by zero, but then the denominator in the formula is a small number.  For this case, as given in Table 2, even after 9 iterations, the Newton-Raphson method does not converge.

Table 2   Division by near zero in Newton-Raphson method.

| Iteration Number |  |  |  |
| --- | --- | --- | --- |
| 0 1 2 3 4 5 6 7 8 9 | 0.019990 –2.6480 –1.7620 –1.1714 –0.77765 –0.51518 –0.34025 –0.22369 –0.14608 –0.094490 | 18.778 –5.5638 –1.6485 –0.48842 –0.14470 –0.042862 –0.012692 –0.0037553 –0.0011091 | 100.75 50.282 50.422 50.632 50.946 51.413 52.107 53.127 54.602 |

Figure 4 Pitfall of division by zero or a near zero number.

3. Oscillations near local maximum and minimum

Results obtained from the Newton-Raphson method may oscillate about the local maximum or minimum without converging on a root but converging on the local maximum or minimum. Eventually, it may lead to division by a number close to zero and may diverge.

For example, for

the equation has no real roots (Figure 5 and Table 3).

Figure 5 Oscillations around local minima for .

Table 3   Oscillations near local maxima and minima in Newton-Raphson method.

| Iteration Number |  |  |  |
| --- | --- | --- | --- |
| 0 1 2 3 4 5 6 7 8 9 | –1.0000 0.5 –1.75 –0.30357 3.1423 1.2529 –0.17166 5.7395 2.6955 0.97678 | 3.00 2.25 5.063 2.092 11.874 3.570 2.029 34.942 9.266 2.954 | 300.00 128.571 476.47 109.66 150.80 829.88 102.99 112.93 175.96 |

4. Root jumping

In some case where the function  is oscillating and has a number of roots, one may choose an initial guess close to a root.  However, the guesses may jump and converge to some other root.  For example for solving the equation  if you choose  as an initial guess, it converges to the root of  as shown in Table 4 and Figure 6.  However, one may have chosen this as an initial guess to converge to .

Table 4   Root jumping in Newton-Raphson method.

| Iteration Number |  |  |  |
| --- | --- | --- | --- |
| 0 1 2 3 4 5 | 7.539822 4.462 0.5499 –0.06307 | 0.951 –0.969 0.5226 –0.06303 | 68.973 711.44 971.91 |

Figure 6 Root jumping from intended location of root for .

Appendix A. What is an inflection point?

For a function , the point where the concavity changes from up-to-down or down-to-up is called its inflection point.  For example, for the function , the concavity changes at  (see Figure 3), and hence (1,0) is an inflection point.

An inflection points MAY exist at a point where  and where  does not exist.  The reason we say that it MAY exist is because if , it only makes it a possible inflection point.  For example, for , , but the concavity does not change at . Hence the point (0, –16) is not an inflection point of .

For , changes sign at  ( for , and  for ), and thus brings up the Inflection Point Theorem for a function  that states the following.

“If  exists and  changes sign at , then the point  is an inflection point of the graph of .”

# Appendix B. Derivation of Newton-Raphson method from Taylor series

Newton-Raphson method can also be derived from Taylor series.  For a general function , the Taylor series is

+

As an approximation, taking only the first two terms of the right hand side,

and we are seeking a point where  that is, if we assume

which gives

This is the same Newton-Raphson method formula series as derived previously using the geometric method.

| NONLINEAR EQUATIONS |  |
| --- | --- |
| Topic | Newton-Raphson Method of Solving Nonlinear Equations |
| Summary | Text book notes of Newton-Raphson method of finding roots of nonlinear equation, including convergence and pitfalls. |
| Major | Civil Engineering |
| Authors | Autar Kaw |
| Date | November 8, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Text boxes

f (x)

f (xi)

f (xi+1)

xi+2

xi+1

xi

x

θ

[xi,  f (xi)]