###### Chapter 08.04

###### Runge-Kutta 4th Order Method for

###### Ordinary Differential Equations

After reading this chapter, you should be able to

- develop Runge-Kutta 4th order method for solving ordinary differential equations,

- find the effect size of step size has on the solution,

- know the formulas for other versions of the Runge-Kutta 4th order method

# What is the Runge-Kutta 4th order method?

Runge-Kutta 4th order method is a numerical technique used to solve ordinary differential equation of the form

So only first order ordinary differential equations can be solved by using the Runge-Kutta 4th order method.  In other sections, we have discussed how Euler and Runge-Kutta methods are used to solve higher order ordinary differential equations or coupled (simultaneous) differential equations.

# How does one write a first order differential equation in the above form?

# Example 1

# Rewrite

in

form.

# Solution

In this case

# Example 2

Rewrite

in

form.

# Solution

In this case

The Runge-Kutta 4th order method is based on the following

(1)

where knowing the value of  at , we can find the value of  at , and

Equation (1) is equated to the first five terms of Taylor series

(2)

Knowing that   and

(3)

Based on equating Equation (2) and Equation (3), one of the popular solutions used is

(4)

(5a)

(5b)

(5c)

(5d)

# Example 3

A rectifier-based power supply requires a capacitor to temporarily store power when the rectified waveform from the AC source drops below the target voltage.  To properly size this capacitor a first-order ordinary differential equation must be solved.  For a particular power supply, with a capacitor of , the ordinary differential equation to be solved is

Using the Runge-Kutta 4th order method, find voltage across the capacitor at .  Use step size .

# Solution

For , ,

is the approximate voltage at

For

is the approximate voltage at

=

Figure 1 compares the exact solution of with the numerical solution using Runge-Kutta 4th order method step size of .

Figure 1 Comparison of Runge-Kutta 4th order method with exact solution for different step sizes.

Table 1 and Figure 2 shows the effect of step size on the value of the calculated temperature at .

Table 1  Value of voltage at time,  for different step sizes.

| Step size, |  |  |  |
| --- | --- | --- | --- |
| 0.00004 0.00002 0.00001 0.000005 0.0000025 | 53.335 26.647 15.986 15.975 15.976 | 37.361 10.673 0.012299 0.00050402 0.0015916 | 233.89 66.817 0.076996 0.0031552 0.0099639 |

Figure 2 Effect of step size in Runge-Kutta 4th order method.

In Figure 3, we are comparing the exact results with Euler’s method (Runge-Kutta 1st order method), Heun’s method (Runge-Kutta 2nd order method) and Runge-Kutta 4th order method.

Figure 3 Comparison of Runge-Kutta methods of 1st, 2nd, and 4th order.

| ORDINARY DIFFERENTIAL EQUATIONS |  |
| --- | --- |
| Topic | Runge-Kutta 4th order method |
| Summary | Textbook notes on the Runge-Kutta 4th order method for solving ordinary differential equations. |
| Major | Electrical Engineering |
| Authors | Autar Kaw |
| Last Revised | November 14, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |