###### Chapter 07.03

###### Simpson’s 1/3 Rule of Integration

After reading this chapter, you should be able to

- derive the formula for Simpson’s 1/3 rule of integration,

- use Simpson’s 1/3 rule it to solve integrals,

- develop the formula for multiple-segment Simpson’s 1/3 rule of integration,

- use multiple-segment Simpson’s 1/3 rule of integration to solve integrals, and

- derive the true error formula for multiple-segment Simpson’s 1/3 rule.

# What is integration?

Integration is the process of measuring the area under a function plotted on a graph.  Why would we want to integrate a function?  Among the most common examples are finding the velocity of a body from an acceleration function, and displacement of a body from a velocity function.  Throughout many engineering fields, there are (what sometimes seems like) countless applications for integral calculus.  You can read about some of these applications in Chapters 07.00A-07.00G.

Sometimes, the evaluation of expressions involving these integrals can become daunting, if not indeterminate.  For this reason, a wide variety of numerical methods has been developed to simplify the integral.  Here, we will discuss Simpson’s 1/3 rule of integral approximation, which improves upon the accuracy of the trapezoidal rule.

Here, we will discuss the Simpson’s 1/3 rule of approximating integrals of the form

where

is called the integrand,

lower limit of integration

upper limit of integration

# Simpson’s 1/3 Rule

The trapezoidal rule was based on approximating the integrand by a first order polynomial, and then integrating the polynomial over interval of integration.  Simpson’s 1/3 rule is an extension of Trapezoidal rule where the integrand is approximated by a second order polynomial.

Figure 1 Integration of a function

## Method 1:

Hence

where  is a second order polynomial given by

.

Choose

and

as the three points of the function to evaluate  and .

Solving the above three equations for unknowns,   and  give

Then

Substituting values of   and  give

Since for Simpson 1/3 rule, the interval  is broken into 2 segments, the segment width

Hence the Simpson’s 1/3 rule is given by

Since the above form has 1/3 in its formula, it is called Simpson’s 1/3 rule.

## Method 2:

Simpson’s 1/3 rule can also be derived by approximating  by a second order polynomial using Newton’s divided difference polynomial as

where

Integrating Newton’s divided difference polynomial gives us

Substituting values of   and  into this equation yields the same result as before

## Method 3:

One could even use the Lagrange polynomial to derive Simpson’s formula.  Notice any method of three-point quadratic interpolation can be used to accomplish this task.  In this case, the interpolating function becomes

Integrating this function gets

Believe it or not, simplifying and factoring this large expression yields you the same result as before

.

## Method 4:

Simpson’s 1/3 rule can also be derived by the method of coefficients.  Assume

Let the right-hand side be an exact expression for the integrals  and .  This implies that the right hand side will be exact expressions for integrals of any linear combination of the three integrals for a general second order polynomial.  Now

Solving the above three equations for   and  give

This gives

The integral from the first method

can be viewed as the area under the second order polynomial, while the equation from Method 4

can be viewed as the sum of the areas of three rectangles.

# Example 1

A company advertises that every roll of toilet paper has at least 250 sheets.  The probability that there are 250 or more sheets in the toilet paper is given by

Approximating the above integral as

- Use Simpson’s 1/3 Rule to find the probability.

- Find the true error,, for part (a).

- Find the absolute relative true error, , for part (a).

# Solution

a)

b)  The exact value of the above integral cannot be found. For calculating the true error and relative true error, we assume the value obtained by adaptive numerical integration using Maple as the exact value.

So the true error is,

Absolute Relative true error,

# Multiple-segment Simpson’s 1/3 Rule

Just like in multiple-segment trapezoidal rule, one can subdivide the interval  into  segments and apply Simpson’s 1/3 rule repeatedly over every two segments.  Note that  needs to be even.  Divide interval  into  equal segments, so that the segment width is given by

.

Now

where

Apply Simpson’s 1/3rd Rule over each interval,

Since

then

# Example 2

A company advertises that every roll of toilet paper has at least 250 sheets.  The probability that there are 250 or more sheets in the toilet paper is given by

Approximating the above integral as

- Use four segment Simpson’s 1/3 Rule to find the probability.

- Find the true error, , for part (a).

- Find the absolute relative true error for part (a).

# Solution

a)  Using  segment Simpson’s 1/3rd Rule,

So

Since

b)  The exact value of the above integral cannot be found. For calculating the true error and relative true error, we assume the value obtained by adaptive numerical integration using Maple as the exact value.

So the true error is

Absolute Relative true error,

Table 2 Values of Simpson’s 1/3 Rule for Example 2 with multiple segments.

Approximate Value % 2 4 6 8 10 0.17907 0.20133 1.0090 1.2042 1.0954 0.79470 0.77244 0.035226 0.23042 0.12167 81.611 79.325 3.6175 23.663 12.495

# Error in Multiple-segment Simpson’s 1/3 rule

The true error in a single application of Simpson’s 1/3rd Rule is given by

In multiple-segment Simpson’s 1/3 rule, the error is the sum of the errors in each application of Simpson’s 1/3 rule.  The error in the n segments Simpson’s 1/3rd Rule is given by

:

:

Hence, the total error in the multiple-segment Simpson’s 1/3 rule is

The term  is an approximate average value of .  Hence

where

| INTEGRATION |  |
| --- | --- |
| Topic | Simpson’s 1/3 rule |
| Summary | Textbook notes of Simpson’s 1/3 rule |
| Major | Industrial Engineering |
| Authors | Autar Kaw, Michael Keteltas |
| Date | November 15, 2012 |
| Web Site | http://numericalmethods.eng.usf.edu |

# Footnotes

The f(4) in the true error expression stands for the fourth derivative of the function f(x).