###### Chapter 03.03

###### Bisection Method of Solving a Nonlinear Equation – More Examples

###### Computer Science

# Example 1

To find the inverse of a value , one can use the equation

where  is the inverse of .

Use the bisection method of finding roots of equations to find the inverse of . Conduct three iterations to estimate the root of the above equation. Find the absolute relative approximate error at the end of each iteration and the number of significant digits at least correct at the end of each iteration.

# Solution

Let us assume

Check if the function changes sign between  and .

Hence

So there is at least one root between   and , that is, between 0 and 1.

## Iteration 1

The estimate of the root is

Hence the root is bracketed between  and , that is, between 0 and 0.5.  So, the lower and upper limits of the new bracket are

At this point, the absolute relative approximate error  cannot be calculated as we do not have a previous approximation.

## Iteration 2

The estimate of the root is

Hence, the root is bracketed between  and , that is, between 0.25 and 0.5. So the lower and upper limits of the new bracket are

The absolute relative approximate error  at the end of Iteration 2 is

None of the significant digits are at least correct in the estimated root of

as the absolute relative approximate error is greater that 5%.

Iteration 3

Hence, the root is bracketed between  and , that is, between 0.375 and 0.5.  So the lower and upper limits of the new bracket are

The absolute relative approximate error,  at the ends of Iteration 3 is

Still none of the significant digits are at least correct in the estimated root of the equation as the absolute relative approximate error is greater than 5%. Seven more iterations were conducted and these iterations are shown in the table below.

Table 1 Root of as a function of the number of iterations for bisection method.

Iteration 1 2 3 4 5 6 7 8 9 10 0 0 0.25 0.375 0.375 0.375 0.39063 0.39844 0.39844 0.39844 1 0.5 0.5 0.5 0.4375 0.40625 0.40625 0.40625 0.40234 0.40039 0.5 0.25 0.375 0.4375 0.40625 0.39063 0.39844 0.40234 0.40039 0.39941 ---------- 100 33.333 14.2857 7.6923 4.00 1.9608 0.97087 0.48780 0.24450 0.25 –0.375 –0.0625 0.09375 0.01563 –0.02344 –3.90625 5.8594 9.7656 –1.4648

At the end of the  iteration,

Hence the number of significant digits at least correct is given by the largest value of  for which

So

The number of significant digits at least correct in the estimated root 0.39941 is 2.

| NONLINEAR EQUATIONS |  |
| --- | --- |
| Topic | Bisection Method-More Examples |
| Summary | Examples of Bisection Method |
| Major | Computer Engineering |
| Authors | Autar Kaw |
| Date | August 7, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |