###### Chapter 04.08

###### Gauss-Seidel Method – More Examples

###### Computer Engineering

# Example 1

To infer the surface shape of an object from images taken of a surface from three different directions, one needs to solve the following set of equations.

The right hand side values are the light intensities from the middle of the images, while the coefficient matrix is dependent on the light source directions with respect to the camera.  The unknowns are the incident intensities that will determine the shape of the object.

Find the values of , , and  using the Gauss-Seidel method. Use

as the initial guess and conduct two iterations.

# Solution

Rewriting the equations gives

## Iteration #1

Given the initial guess of the solution vector as

we get

The absolute relative approximate error for each  then is

At the end of the first iteration, the estimate of the solution vector is

and the maximum absolute relative approximate error is .

## Iteration #2

The estimate of the solution vector at the end of Iteration #1 is

Now we get

The absolute relative approximate error for each  then is

At the end of the second iteration, the estimate of the solution vector is

and the maximum absolute relative approximate error is .

Conducting more iterations gives the following values for the solution vector and the corresponding absolute relative approximate errors.

| Iteration |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1 2 3 4 5 6 | 1058.6 –2117.0 4234.8 –8470.1 16942 –33888 | 99.055 150.00 149.99 150.00 149.99 150.00 | 1062.7 –2112.9 4238.9 –8466.0 16946 –33884 | 99.059 150.295 149.85 150.07 149.96 150.01 | –783.81 803.98 –2371.9 3980.5 –8725.7 16689 | 101.28 197.49 133.90 159.59 145.62 152.28 |

After six iterations, the absolute relative approximate errors are not decreasing. In fact, conducting more iterations reveals that the absolute relative approximate error does not approach zero but approaches .

| SIMULTANEOUS LINEAR EQUATIONS |  |
| --- | --- |
| Topic | Gauss-Seidel Method – More Examples |
| Summary | Examples of the Gauss-Seidel method |
| Major | Computer Engineering |
| Authors | Autar Kaw |
| Date | August 8, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |