###### Chapter 05.02

###### Direct Method of Interpolation – More Examples

###### Electrical Engineering

# Example 1

Thermistors are used to measure the temperature of bodies. Thermistors are based on materials’ change in resistance with temperature. To measure temperature, manufacturers provide you with a temperature vs. resistance calibration curve. If you measure resistance, you can find the temperature. A manufacturer of thermistors makes several observations with a thermistor, which are given in Table 1.

Table 1  Temperature as a function of resistance.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |
| --- | --- |

Figure 1 Resistance vs. temperature.

Determine the temperature corresponding to 754.8 ohms using the direct method of interpolation and a first order polynomial.

# Solution

For first order polynomial interpolation (also called linear interpolation), we choose the temperature given by

Figure 2 Linear interpolation.

Since we want to find the temperature at , and we are using a first order polynomial, we need to choose the two data points that are closest to  that also bracket  to evaluate it.  The two points are  and .

Then

gives

Writing the equations in matrix form, we have

Solving the above two equations gives

Hence

At ,

# Example 2

Thermistors are used to measure the temperature of bodies. Thermistors are based on materials’ change in resistance with temperature. To measure temperature, manufacturers provide you with a temperature vs. resistance calibration curve. If you measure resistance, you can find the temperature. A manufacturer of thermistors makes several observations with a thermistor, which are given in Table 2.

Table 2  Temperature as a function of resistance.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |
| --- | --- |

Determine the temperature corresponding to 754.8 ohms using the direct method of interpolation and a second order polynomial. Find the absolute relative approximate error for the second order polynomial approximation.

# Solution

For second order polynomial interpolation (also called quadratic interpolation), we choose the temperature given by

Figure 3 Quadratic interpolation.

Since we want to find the temperature at  and we are using a second order polynomial, we need to choose the three data points that are closest to  that also bracket  to evaluate it. The three points are,  and .

Then

gives

Writing the three equations in matrix form, we have

Solving the above three equations gives

Hence

At ,

The absolute relative approximate error  obtained between the results from the first and second order polynomial is

# Example 3

Thermistors are used to measure the temperature of bodies. Thermistors are based on materials’ change in resistance with temperature. To measure temperature, manufacturers provide you with a temperature vs. resistance calibration curve. If you measure resistance, you can find the temperature. A manufacturer of thermistors makes several observations with a thermistor, which are given in Table 3.

Table 3  Temperature as a function of resistance.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 |
| --- | --- |

- Determine the temperature corresponding to 754.8 ohms using the direct method of interpolation and a third order polynomial. Find the absolute relative approximate error for the third order polynomial approximation.

- The actual calibration curve used by industry is given by

Substituting  and  the calibration curve is given by

Table 4  Manipulation for the given data.

| 1101.0 911.3 636.0 451.1 | 25.113 30.131 40.120 50.128 | 7.0040 6.8149 6.4552 6.1117 | 0.039820 0.033188 0.024925 0.019949 |
| --- | --- | --- | --- |

Find the calibration curve and use it to find the temperature corresponding to 754.8 ohms.  What is the difference between the results from part (a)?  Is the difference larger using results from part (a) or part (b), if the actual measured value at 754.8 ohms is 35.285?

# Solution

a) For third order polynomial interpolation (also called cubic interpolation), we choose the temperature given by

Figure 4 Cubic interpolation.

Since we want to find the temperature at , and we are using a third order polynomial, we need to choose the four data points closest to  that also bracket  to evaluate it. The four points are , ,  and .

Then

gives

Writing the four equations in matrix form, we have

Solving the above four equations gives

Hence

The absolute relative approximate error  for the results from the second and third order polynomial is

b) Finding the cubic interpolant using the direct method for

Requires that we first calculate the new values of  and .

| 7.0040 6.8149 6.4552 6.1117 | 0.039820 0.033188 0.024925 0.019949 |
| --- | --- |

Then

gives

Writing the four equations in matrix form, we have

Solving the above four equations gives

Hence

However, since  and  we get

or

At ,

Since the actual measured value at 754.8 ohms is  the absolute relative true error between the value used for part (a) is

and for part (b) is

Therefore, the direct method of cubic polynomial interpolation, that is,

obtained more accurate results than the actual calibration curve of

| INTERPOLATION |  |
| --- | --- |
| Topic | Direct Method of Interpolation |
| Summary | Examples of direct method of interpolation. |
| Major | Electrical Engineering |
| Authors | Autar Kaw |
| Date | August 12, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |