###### Chapter 06.04

###### Nonlinear Models for Regression-More Examples

###### Electrical Engineering

# Example 1

To be able to draw road networks from aerial images, light intensities are measured at different pixel locations. The following intensities are given as a function of pixel location.

Table 1 Light intensities as a function of pixel location.

Pixel Location, Intensity, −3 119 −2 165 −1 231 0 243 1 244 2 214 3 136

Regress the above data to a second order polynomial

# Solution

Table 2 shows the summations needed for the calculation of the constants of the regression model.

Table 2 Summations for calculating constants of model.

Pixel Location, Intensity, 1 −3 119 9 −27 81 −357 1071 2 −2 165 4 −8 16 −330 660 3 −1 231 1 −1 1 −231 231 4 0 243 0 0 0 0 0 5 1 244 1 1 1 244 244 6 2 214 4 8 16 428 856 7 3 136 9 27 81 408 1224 0 1352 28 0 196 162 4286

is the quadratic relationship between the pixel location and intensity where the coefficients , ,  are found as follows

We have

Solve the above system of simultaneous linear equations, we get

The polynomial regression model is

Figure 1 Second order polynomial regression model for intensity as a function of pixel location.