###### Chapter 08.04

###### Runge-Kutta 4th Order Method for Ordinary Differential Equations-More Examples

###### Industrial Engineering

# Example 1

The open loop response, that is, the speed of the motor to a voltage input of 20V, assuming a system without damping is

.

If the initial speed is zero  ,and using the Runge-Kutta 4th order method, what is the speed at ?  Assume a step size of .

# Solution

For , ,

is the approximate speed of the motor at

For

is the approximate speed of the motor at

=

The exact solution of the ordinary differential equation is given by

The solution to this nonlinear equation at  is

rad/s

Figure 1 compares the exact solution with the numerical solution using the Runge-Kutta 4th order method using different step sizes.

Figure 1 Comparison of Runge-Kutta 4th order method with exact solution for different step sizes.

Table 1 and Figure 2 show the effect of step size on the value of the calculated speed of the motor at .

Table 1  Values of speed of the motor at 0.8 seconds for different step sizes.

| Step size, |  |  |  |
| --- | --- | --- | --- |
| 0.8 0.4 0.2 0.1 0.05 | 147.20 299.54 302.96 303.09 303.09 | 155.89 3.5535 0.12988 0.0062962 0.00034702 | 51.434 1.1724 0.042852 0.0020773 0.00011449 |

Figure 2 Effect of step size in Runge-Kutta 4th order method.

In Figure 3, we are comparing the exact results with Euler’s method (Runge-Kutta 1st order method), Heun’s method (Runge-Kutta 2nd order method) and the Runge-Kutta 4th order method.

Figure 3 Comparison of Runge-Kutta methods of 1st, 2nd, and 4th order.