###### Chapter 05.05

###### Spline Method of Interpolation – More Examples

###### Mechanical Engineering

# Example 1

For the purpose of shrinking a trunnion into a hub, the reduction of diameter  of a trunnion shaft by cooling it through a temperature change of  is given by

where

original diameter

coefficient of thermal expansion at average temperature

The trunnion is cooled from  to , giving the average temperature as .  The table of the coefficient of thermal expansion vs. temperature data is given in Table 1.

Table 1  Thermal expansion coefficient as a function of temperature.

| Temperature, | Thermal Expansion Coefficient, |
| --- | --- |
| 80 | 6.47 |
| 0 | 6.00 |
| –60 | 5.58 |
| –160 | 4.72 |
| –260 | 3.58 |
| –340 | 2.45 |

Figure 1 Thermal expansion coefficient vs. temperature.

If the coefficient of thermal expansion needs to be calculated at the average temperature of , determine the value of the coefficient of thermal expansion at  using linear splines.

# Solution

Since we want to find the coefficient of thermal expansion at  and we are using linear splines, we need to choose the two data points that are closest to  that also bracket  to evaluate it. The two points are  and .

Then

gives

Hence

At

Linear spline interpolation is no different from linear polynomial interpolation. Linear splines still use data only from the two consecutive data points. Also at the interior points of the data, the slope changes abruptly. This means that the first derivative is not continuous at these points.  So how do we improve on this? We can do so by using quadratic splines.

# Example 2

For the purpose of shrinking a trunnion into a hub, the reduction of diameter  of a trunnion shaft by cooling it through a temperature change of  is given by

where

original diameter

coefficient of thermal expansion at average temperature

The trunnion is cooled from  to , giving the average temperature as .  The table of the coefficient of thermal expansion vs. temperature data is given in Table 2.

Table 2  Thermal expansion coefficient as a function of temperature.

| Temperature, | Thermal Expansion Coefficient, |
| --- | --- |
| 80 | 6.47 |
| 0 | 6.00 |
| –60 | 5.58 |
| –160 | 4.72 |
| –260 | 3.58 |
| –340 | 2.45 |

- Determine the value of the coefficient of thermal expansion at  using quadratic splines. Find the absolute relative approximate error for the second order approximation.

- The reduction of the diameter is given more accurately by

where     room temperature

temperature of cooling medium

Given

find a better estimate. What is the difference between the value found in part (a) and part (b)?

Solution

a) Since there are six data points, five quadratic splines pass through them.

The equations are found as follows.

1. Each quadratic spline passes through two consecutive data points.

passes through  and .

(1)

(2)

passes through  and .

(3)

(4)

passes through  and .

(5)

(6)

passes through  and .

(7)

(8)

passes through  and .

(9)

(10)

2. Quadratic splines have continuous derivatives at the interior data points.

At

(11)

At

(12)

At

(13)

At

(14)

3.  Assuming the first spline  is linear,

(15)

Solving the above 15 equations gives the 15 unknowns as

| 1 | 0 | 0.014125 | 7.2525 |
| --- | --- | --- | --- |
| 2 | –2.725 | –4.5 | 5.4104 |
| 3 | –7.5 | 0.008435 | 6.0888 |
| 4 | –2.5417 | 0.005475 | 6 |
| 5 | 5 | 0.005475 | 6 |

Therefore, the splines are given by

At

The absolute relative approximate error  obtained between the results from the linear and quadratic splines is

b) The reduction of the diameter is given more accurately by

where

room temperature

boiling temperature of liquid nitrogen

Given

To find  we can integrate the quadratic splines with respect to temperature.

To compare this result with our results from part (a), we take the average coefficient of thermal expansion over this interval, given by:

The absolute relative approximate error  obtained between the results from part (a) and part (b) is