###### Chapter 08.02

###### Euler’s Method for Ordinary Differential Equations-More Examples

###### Mechanical Engineering

# Example 1

A solid steel shaft at room temperature of  is needed to be contracted so that it can be shrunk-fit into a hollow hub.  It is placed in a refrigerated chamber that is maintained at .  The rate of change of temperature of the solid shaft  is given by

Using Euler’s method, find the temperature of the steel shaft after 86400 seconds.  Take a step size of  seconds.

# Solution

The Euler’s method reduces to

For , ,

is the approximate temperature at

For , ,

is the approximate temperature at

Figure 1 compares the exact solution with the numerical solution from Euler’s method for the step size of .

Figure 1 Comparing exact and Euler’s method.

The problem was solved again using smaller step sizes.  The results are given below in

Table 1.

Table 1  Temperature at 86400 seconds as a function of step size, .

| Step size, |  |  |  |
| --- | --- | --- | --- |
| 86400 43200 21600 10800 5400 | 153.52 463.32 29.542 27.795 26.958 | 127.42 437.22 3.4421 1.6962 0.85870 | 488.21 1675.2 13.189 6.4988 3.2902 |

Figure 2 shows how the temperature varies as a function of time for different step sizes.

Figure 2 Comparison of Euler’s method with exact solution for different step sizes.

While the values of the calculated temperature at  as a function of step size are plotted in Figure 3.

Figure 3 Effect of step size in Euler’s method.

The solution to this nonlinear equation at is

# Text boxes

h=240