###### Chapter 04.06

###### Gaussian Elimination – More Examples

###### Electrical Engineering

# Example 1

Three-phase loads are common in AC systems. When the system is balanced the analysis can be simplified to a single equivalent circuit model. However, when it is unbalanced the only practical solution involves the solution of simultaneous linear equations. In one model the following equations need to be solved.

Find the values of , , , , , and  using naïve Gauss elimination.

# Solution

# Forward Elimination of Unknowns

Since there are six equations, there will be five steps of forward elimination of unknowns.

First step

Divide Row 1 by 0.7460 and multiply it by 0.4516, that is, multiply Row 1 by .

Subtract the result from Row 2 to get

Divide Row 1 by 0.7460 and multiply it by 0.0100, that is, multiply Row 1 by .

Subtract the result from Row 3 to get

Divide Row 1 by 0.7460 and multiply it by 0.0080, that is, multiply Row 1 by .

Subtract the result from Row 4 to get

Divide Row 1 by 0.7460 and multiply it by 0.0100, that is, multiply Row 1 by .

Subtract the result from Row 5 to get

Divide Row 1 by 0.7460 and multiply it by 0.0080, that is, multiply Row 1 by .

Subtract the result from Row 6 to get

Second step

Divide Row 2 by 1.0194 and multiply it by −0.0019464, that is, multiply Row 2 by .

Subtract the result from Row 3 to get

Divide Row 2 by 1.0194 and multiply it by 0.014843, that is, multiply Row 2 by .

Subtract the result from Row 4 to get

Divide Row 2 by 1.0194 and multiply it by −0.0019464, that is, multiply Row 2 by .

Subtract the result from Row 5 to get

Divide Row 2 by 1.0194 and multiply it by 0.014843, that is, multiply Row 2 by .

Subtract the result from Row 6 to get

Third step

Divide Row 3 by 0.77857 and multiply it by 0.52036, that is, multiply Row 3 by .

Subtract the result from Row 4 to get

Divide Row 3 by 0.77857 and multiply it by 0.0098697, that is, multiply Row 3 by .

Subtract the result from Row 5 to get

Divide Row 3 by 0.77857 and multiply it by 0.0078644, that is, multiply Row 3 by .

Subtract the result from Row 6 to get

Fourth step

Divide Row 4 by 1.1264 and multiply it by −0.0012679, that is, multiply Row 4 by .

Subtract the result from Row 5 to get

Divide Row 4 by 1.1264 and multiply it by 0.015126, that is, multiply Row 4 by .

Subtract the result from Row 6 to get

Fifth step

Divide Row 5 by 0.80775 and multiply it by 0.60375, that is, multiply Row 5 by .

Subtract the result from Row 6 to get

The six equations are

# Back Substitution

From the sixth equation

Substituting the value of  in the fifth equation,

Substituting the value of  and  in the forth equation,

Substituting the value of ,  and  in the third equation,

Substituting the value of , ,  and  in the second equation,

Substituting the value of , , , , and  in the first equation,

Hence the solution vector is

| SIMULTANEOUS LINEAR EQUATIONS |  |
| --- | --- |
| Topic | Gaussian Elimination – More Examples |
| Summary | Examples of Gaussian elimination |
| Major | Electrical Engineering |
| Authors | Autar Kaw |
| Date | June 15, 2010 |
| Web Site | http://numericalmethods.eng.usf.edu |